## Slide 1: ISB & SIB Annual Refresher Training
Draft Annual Refresher
03 Aug 2023
Notes: Welcome to the ISB & SIB Annual refresher training course

## Slide 2: Overview
Training Requirements
Initial Response / Incident Commander Responsibilities
Interim Safety Board (ISB) Responsibilities
Safety Investigation Board (SIB) Process
The Safety Report
Notes: This is what we will cover today.

## Slide 3: DAFI 91-204
Training Requirements
Paragraph 2.12.2.1.
  Provide annual refresher training on the basics of mishap investigation to personnel trained and qualified to perform ISB/SIB duties (AFRC will only train personnel for interim board participation per MOA/MOUs with the closest Regular AF installation).
Paragraph 2.12.2.2.
  Include available human factors experts (e.g., aerospace physiologists, psychologists, flight surgeons) who have completed either the Aircraft Mishap Investigation and Prevention workshop, Aircraft Mishap Investigation Course, Mishap Investigation Non-Aviation course, or Introduction to Mishap Investigation course in annual refresher training. (T-1) Annually track human factors experts for completion of training and availability to support ISBs and SIBs. (T-1)
Notes: Why are we here? DAFI 91-204 requires annual training for all potential primary board members and Human factors experts that may sit on a SIB.

## Slide 4
Initial Response
Notes: We’ll start at the beginning…. A mishap and how we respond

## Slide 5: Following a Mishap
IAW DAFI 91-204, Paragraph 2.6., The Commander of the Regular Air Force / or Space Force installation nearest a mishap will:
  Respond to the mishap
  Activate the disaster response force
  Appoint an incident commander
  Appoint an ISB to preserve evidence
  Conduct toxicology (TOX) testing as required
  Make appropriate military and civilian notifications
  For ground mishaps WG/SE will likely fill ISB role
  Likely be initial host for SIB
Some mishaps may require multiple ISBs
Notes: Following all AF mishaps, the base nearest (regardless of branch of service) to the mishap site has the responsibility to respond.
Air Reserve Component (ARC) (AF Reserve and ANG) installations:
For Class As - If nearest the mishap, will respond with available resources to the maximum extent possible, in coordination with the responding Regular AF installation.
For Class Bs - will normally be able to handle everything
Vice Versa, if a Navy F-18 is coming into your base and crashes, you’ll respond and set up an ISB.
The ISB will normally come from the Wing closest to the mishap location.
In the case of most occupational mishaps, WG/SE will fulfill the duties of the ISB until the SIB arrives.
Some mishaps may require 2 ISBs.
An example: Let’s say an F-16 out of Nellis crashes while on approach here at XYZ AF/SF Base. Here at XYZ AF/SF Base you will begin the response process but there will be two ISBs; one here at XYZ AF/SF Base and the second will be going on concurrently at Nellis, more on this later.
Here at XYZ AF/SF Base you will likely host the SIB since this is where the mishap occurred. More on this later.

## Slide 6: Following a Mishap
CC’s Senior Staff or ICC
Disaster Response Force
Wing/Safety
Delta/Safety
Interim Safety Board
Initiates Disaster Response Actions, Appoints the ISB,
Etc.
Emergency Ops Center
First Responders & Emergency Responders
Respond to the Site
Sends out Preliminary Reports, is the POC for the ISB
Gathers and Preserves Evidence
Notes: This is simplistic, but there are basically 4 things going on at roughly the same time following a major mishap

## Slide 7: Disaster Response Force
First Responders typically include:
  Search and Rescue: provide search / rescue / recovery support
  Fire Fighters: fight any fires
  Medical: treat injured persons
  Security Forces: cordon the site
  EOD: secure the hazards
Notes: The Fire Chief is initially the Incident Commander (IC) at the site.
Typical response will come in three waves
This shows the typical “first wave” of responders to the crash site and their responsibilities.
FR = First Responders (AFI 10-2501 First Responders are members of the DRF elements that deploys immediately to the disaster scene to provide initial C2, to save lives, and to suppress and control hazards. Firefighters, law enforcement and security personnel, key emergency medical personnel provide the initial, immediate response to major accidents, natural disasters, and CBRNE incidents.

## Slide 8: Disaster Response Force
Emergency responders (Follow-on Element)
  Respond directly to pre-planned assembly point and await words from the IC (Incident Commander)
    Photographer
    Civil Engineer
    Public Affairs
    Flight Safety Officer (for flight mishap)
  Support Response
    Respond when IC requests their presence
    Mortuary Affairs
    Transportation
    Chaplain
Notes: After the site’s been made safe by the First responders, the following individuals may become involved.
ER = Emergency Responders (AFI 10-2501 Emergency Responders are members of the DRF response elements that deploy after the First Responders to expand C2 and provide additional support.
These may depend on the where and what of the mishap. What if it’s in 2000’ of water? (rhetorical)
The Support responders are such “support” and respond when needed.
Also, you may want to think about a legal representative as well at the site (especially concerning property damages, etc.).

## Slide 9: Crash Site
Crash Site & Wreckage Authority:
  Fire Chief – Rescue/Fire, Initial Response
  Incident Commander/Recovery Operations Chief
    EOD, HAZMAT, Bio-Environmental
  Interim Safety Board
    Document and Preserve
    Crash Recovery (If necessary)
  Safety Investigation Board
    Crash Recovery (Most likely)
Notes: The ROC or IC “owns” the mishap site, the ISB “owns” the mishap aircraft for flight mishaps. Close coordination is required between the two.
DAFI91-204, paragraph 7.2.5.1. states, “Once the mishap site is safe, the ISB will accept control of the wreckage and/or evidence, as applicable.”
The ISB President, Investigating Officer or Chief of Safety will not perform duties as IC or ROC.”
------
Again, the IC is responsible for the site and actions at the site.
Recent change to AFMAN 10-2502 Chapter 4 added a Recovery Operations Chief (ROC) as a follow on to the IC during the SIB phase to lead Recovery Ops. May be the same individual.

## Slide 10: Recovery Operations Chief & Incident Commander
Recovery Operations Chief (ROC)
  The fire chief or senior on‑duty fire fighter is in command of the mishap scene until the fire is extinguished and rescue efforts are complete
  Responsibilities include:
    Fire and damage control
    Rescue
    First aid
    Emphasis on recovery and treatment of survivors
Incident Commander (IC)
  The fire chief then briefs the IC on the mishap site status
  The IC then assumes control of the mishap scene
  *Normally, the IC will not assume control of the scene until it is declared safe
Notes: Okay, who declares the site safe? The Fire Chief - think of him as the initial IC
The initial first responder on scene will establish command and perform IC duties until replaced by a more competent or higher trained IC. If the incident requires other agencies to respond to the incident, then the incident commander must have the appropriate training and experience as an IC.
He then turns the site over to the assigned IC…
The Incident Commander is a trained and experienced responder that provides on-scene tactical control using subject matter experts (SME) and support from other functions. The Fire and Emergency Services (FES) will be the incident commander for all incidents involving two or more response agencies. The initial First Responder will assume the IC position until the senior FES person arrives on scene. Once on scene, command is formally transferred from the initial First Responder to the senior FES person. For example, Security Forces responds to a hostage situation and the senior security forces member will assume IC until FES arrives on scene. Then SF briefs the senior FES person and transfers command. The SF person then assumes the operations branch chief position to provide direct tactical operational support to the IC.
AFI 10-2501, Emergency Management Program, Table 5.1 states, “The Incident Commander must be experienced in incidents of the appropriate type and complexity. They must meet the training requirements outlined in Chapter 4, including training to manage multiple agency responses, if required. The Incident Commander must be certified before establishing and or assuming command of a HAZMAT incident.” (T-2).
Note: ANG FES serves as the IC on all ANG multiple agency responses.
ISB/SIB BPs are not IC or ROC

## Slide 11
Interim Safety Board Responsibilities

## Slide 12: ISB Responsibilities
Overall Responsibilities
  Convened For Class A & B On-duty Mishaps
  Convened at Wing Level
  Convened at the location where the mishap occurred
  At the wing which is the owning organization for the personnel or equipment
  Gather and Preserve Evidence
  Does NOT determine mishap cause
  Not called “Interim Safety Investigation Board”
Notes: Mentioned previously could have several ISBs going on at once (base that owned the asset, base where mishap occurred)
Emphasis Bullet
The ISB does not determine mishap cause – it is not called the “Interim Safety Investigation Board”
Restrict work to collection, protection, and preservation of evidence, not determining cause. That is the SIB’s job.

## Slide 13: ISB Responsibilities
Major Responsibilities
  Assume “control” of the mishap wreckage
    *Do not assume control of the mishap site
    Preserve perishable evidence
  Gather and secure ops, MX, medical evidence, etc.
  Make initial determination of mishap category
  Accomplish preliminary mishap reporting
  Photograph mishap site, wreckage, human remains
  Conduct initial interviews – gathering the “what happened?” information
  Initial site diagram
  Prepare for arrival of the Safety Investigation Board (and the Wing / Safety or Delta / Safety)
Notes: Remember IC “controls” the site, but the ISB has specific functions too.
We’ll discuss each one in the following slides.

## Slide 14: ISB Procedures
Should be outlined in the Wing’s Incident Emergency Response Plans (IEMP 10-2) and should describe the responsibilities of and provide checklists for each element to which tasks will be assigned or from which support will be required, including:
  The Incident Commander
  Wing/Safety or Delta/Safety
  All Interim Safety Board members, by position
  PA
  Chaplin
  JA
  CE
  WX
  SG
  Etc.
Notes: What used to be the (Mishap Response Plan) MRP is now called the (Installation Emergency Management Plan) IEMP 10-2
These are exercised in the Base (Major/Mass Accident Response Exercise) MAREs.
Note: Wing IEMP 10-2 and/or MRP is common verbiage

## Slide 15: ISB Responsibilities
Responsibilities are covered in:
  DAFI 91-204, Paragraph 2.7. The ISB President or Investigating Officer
  DAFI 91-204, Paragraph 2.8. The ISB
  DAFMAN 91-222, Paragraph 2.6. Interim Safety Board President
  Local Wing or Delta Mishap Response Plan
Notes: ISB responsibilities are covered in DAFI 91-204.
Example shown is fictitious
Wing/Delta SE is OPR
Wing/Delta MRP has checklists for all ISB members and wing agencies and instructions on what to accomplish following a mishap

## Slide 16
FLIGHT
ISB GENERAL
INFORMATION
GROUND
WEAPONS
Notes: This is a copy of the Mishap Response Plan (MRP) from the AZ Air National Guard.
This real-world example does not have a space example, given that the AZ National Guard does not have a space mission. All SFBs will have space-appropriate MRPs.

## Slide 17: ISB Procedures
Notes: Two example checklists from (AZANG)162nd MRP
One for the Mission Support Group Commander ISB – a checklist
One fore the Board President ISB checklist – a checklist
Any checklists are to be filled in and turned over to SIB to document all actions taken by the ISB
*Review checklist for each member:
-Recorder

## Slide 18
Determining Mishap Class

## Slide 19: Mishap Class
Determine mishap costs by adding all reportable damage, injury, etc.
  Work with Wing / Safety or Delta / Safety and the Convening Authority Safety
Only direct cost (vs. indirect costs) are used to determine mishap classification - direct costs include:
  Actual cost of repair or replacement
  Actual cost of all damaged or destroyed property
  DOD and Non-DoD assets
  Injury / illness cost associated with the mishap
  Environmental cleanup costs
  Current repair costs for field-level and depot-level repairs can be found on the AFSEC Portal
    AFSEC Home
Notes: This applies to all mishaps: flight, ground, space, and weapons.
Only direct cost (vs indirect costs) are used to determine mishap classification
Current repair costs for field and depot level repairs can be found on the AFSEC Portal page

## Slide 20: Mishap Class
AFSEC Portal
  Search for “mishap cost”
  At the bottom of the page, look for the U.S. Air Force Mishap and Event Classifications section
  AFSEC Home
Notes: Mishap Investigation Process (af.mil)

## Slide 21: Mishaps Requiring a SIB
Class A – One or more of the following:
  Direct cost of $2,500,000 or more
  Fatality or permanent total disability
  Destroyed aircraft
  Permanent loss of primary mission capability of a DAF space vehicle
  Class B – One or more of the following:
  Direct cost of $600,000 – to $2,500,000
  Permanent partial disability
  Hospitalization of three or more people
  Permanent degradation of primary or secondary mission capability of a DAF space vehicle or the permanent loss of secondary mission capability of a DAF space vehicle
Notes: Let’s review the Mishap Classes before we start
All services use the same DOD standard

## Slide 22
Mishap Site Actions

## Slide 23: Mishap Site Actions
Every situation is different
Access after site is declared “Safe” by the Incident Commander
  Fire safe
  EOD safe
  Security cordon
  Other hazards
    Pressure vessels
    Environmental hazards
    Bioenvironmental hazards
Notes: Be it a weapons mishap, a forklift accident, or a plane crash - any hazardous situation must be declared safe before the ISB can start their work.
Remember the ISB doesn’t “control” the mishap site
You want the site to be declared safe before ISB begins their job…what defines safe?
Can a site ever be 100% safe?

## Slide 24: Priority Considerations
Responders
Declare the site “safe”
Survivor recovery
Site security
Human remains
Initial site survey (stakes)
Site logistics
Establish communications
Weather observation
Secure any classified data / material
ISB
Flight Data / Data Recorders
Witnesses / Survivor statements
Equipment fluids (Hyd, fuel, oil, LOX)
Impound records
Preservation of perishable evidence
Photography
Notes: These are the ISBs and responder considerations/priority.
*The top three actions indicate dual responsibility
- Responders and SIB accomplish jointly
*This list is not all inclusive

## Slide 25: Mishap Site Actions
Initial walk through
Photograph mishap site
Preserve perishable on site evidence
  Protect wreckage – consider the weather
  Ground markings / impact marks
Witness identification
  Locate and interview transient witnesses
Preliminary diagram of major components
Notes: Actions ISB typically accomplishes at the crash site.

## Slide 26: Mishap Site Actions
Mishap site Do’s and Don’ts
  DON’T
    Trample the site
    Move wreckage needlessly
    Put fractured parts back together
    Stick your hands in dark places
  DO
    Identify parts and diagram mishap site
    Know the site hazards and use proper PPE
    Preserve site evidence to max extent possible
    Ensure all wreckage and ground scars are photographed from all angles
    Take engine, fuel, hydraulic and liquid oxygen (LOX) samples
    Establish a personnel roster to limit access to site
Notes: Most are applicable regardless of mishap category, except maybe space - Several are flight specific
  Emphasize: Do establish a personnel roster to limit access to site
Add: Limit/control photography (no cell phone cameras, etc.)

## Slide 27: Mishap Site Actions
Fatalities
  Remains tagged, photographed and removed
  Involve your Flight Surgeon with Mortuary Affairs Officer and Coroner
  With large, complex mishaps this process may take days
Data recorders
  Contact AFSEC / Technical Assistance (DSN 246-5867) to determine:
    Where to locate the devices
    How to download the data
    Where to send recorders
    Where to locate other sources of data
Notes: Despite the fact we say “don’t disturb the wreckage” there are 3 things we ask the ISB to accomplish before SIB arrival
1. Fatalities/HR removed
2. Pull the FDR/CVR if so equipped. Call AFSEC to figure out where to ship
3. Fluid samples taken from aircraft. (Hyd, engine oil, O2 sample, etc.). Call AFSEC to figure out where to ship
For each of these steps document the changes to aircraft configuration and what you are doing.
4. Don’t let local MX take stuff off the aircraft or download data w/o talking to AFSEC

## Slide 28: Mishap Site Actions
Regarding internal recorders, if part of the wreckage:
  Do NOT allow anyone to review data acquired from the recording devices that have been recovered from wreckage
    This includes Wing/CCs, Ops Group/CCs, and Squadron/CCs, etc.
  Until this equipment can be sent to AFSEC, store it (them) in the SIB room or vault where other wreckage and equipment recovered from the mishap is stored
  Once the SIB has arrived on site, transfer the equipment over to them
  The SIB may then choose to send the recording device(s) to AFSEC for analysis – following proper coordination before shipping
Notes: Despite the fact we say “don’t disturb the wreckage” there are 3 things we ask the ISB to accomplish before SIB arrival…………..
1. Fatalities/HR removed
2. Pull the FDR/CVR if so equipped. Call AFSEC to figure out where to ship With FDRs you expect to find the box on the left, more than likely you will just find the CSMU portion as shown on the right.
3. Fluid samples taken from aircraft. (Hyd, engine oil, O2 sample, etc.). Call AFSEC to figure out where to ship
For each of these steps document the changes to aircrafts configuration and what you are doing.

## Slide 29: Initial Walk Through
Missing Wing
*Flight Mishap Example
Notes: On the initial site walk through ensure all the required parts are present. In this flight example a wing is missing. We’ll need to launch a search to find it.
Also, look for things in the wreckage that are present but should not be (like a screwdriver in the wreckage, etc.)

## Slide 30: Initial Walk Through
Notes: Is the site safe should be one of our primary concerns.
In this example what is the status of the power lines and how stable are the cranes?
Work with the IC to know the hazards.

## Slide 31: Initial Walk Through
Know what hazards you are dealing with!
Use Personal Protective Equipment (PPE) if required
Limit access to site, brief all on hazards
Responsibility of IC to know the site hazards, know the PPE requirements, and provide PPE to individuals
Notes: Although the ISB dealt with site hazards initially, many may still exist when the SIB arrives.
HAZMAT might be partially cleaned up by the time SIB arrives, blood borne pathogens might be minimized after remains removed, etc.
However, you should always consider the environment
Picture shows HAZMAT clean up of F-16 impact crater….do we need to dress like this?

## Slide 32: Site Hazards
Hazardous materials
Hazardous situations
Safety Board Members are NOT experts in Hazard recognition and removal
Rely on the EXPERTS to…
Perform a RM Analysis of the mishap site

## Slide 33: Stake the Wreckage
Notes: Q: What are the hazards here?
A: Building fire

## Slide 34: Stake the Wreckage
Notes: Weapons Class B, 20 NOV 2012, Convening Authority: Air Force Materiel Command $571,000.00
On 30 Oct 12, Aerojet contracted with Arnold Engineering Development Complex (AEDC) to x-ray a Large Class Stage 2 (LCS2) solid rocket motor to verify the structural integrity of the LCS2 before proceeding to static fire. The loaded container rolled out of the slings and impacted
the floor during unloading from trailer.
Possible issues/Hazards? Trailer stability, further shifting of load.
Plus (see next slide)

## Slide 35: Stake the Wreckage
Visible stakes
Color coding
  Paint
  Ribbons
Tags
  What items need staking?
  What to diagram?
  What do the colors designate?
Notes: Some considerations pertaining to the staking of wreckage:
Can use stakes, paint, etc.
Different color stakes to represent different things.
Yellow might = aircraft parts, orange might = human remains
Can put #s on flags to assist with diagraming the site
*Above image is of a mishap involving a Hill F-16 engine failure, May 2012, crashed on UTTR

## Slide 36: Photography
Purpose
  Documents the mishap
  Educates people who could not observe the scene firsthand
  Enhances understanding in briefings and the report
Rules of thumb
  Overshoot – take more photos than you think you’ll need
  Document each photograph!!!
    So that you will not forget what is captured
Control of pictures
  Personal / cell phone cameras are NOT allowed
  Must control mishap related information and sharing
Notes: One of the ISBs primary functions
One of investigators most useful tools to document site, for reports, briefings, etc.
Emphasize Bullets:
Rules of Thumb
Overshoot …….shoot pictures of everything, its all digital anyway, only using up disk space
Document each photograph!!!.....going to be shooting thousands of photos. Later you’ll wonder what some the photos were
Note pad, GPS, somebody from MX to help ID parts, # board, etc.
Control the pictures
Don’t allow Personal/cell phone cameras……
Only official photographer and members of ISB

## Slide 37: Photography
“Perishable” to “Non-Perishable”
Generic time-sensitive list:
  Medical evidence
  Potentially significant evidence
    Ground scars, etc.
  Aerial photography
  Wreckage inventory
  Damage to private property
  Witness point-of-view shots

## Slide 38: Photography
What are we looking at?
Document each photo!!!
Notes: Ways to document
What is it and where was it found?
Flag helps to identify part in photo, inventory list of what flag is what
MX can help you identify parts in the debris field
“GPS located next to “alpha” part”

## Slide 39: Murphy’s Law
…of photography
The chances of a piece of evidence having been measured and photographed before someone alters it is inversely proportional to its importance in determining why the mishap occurred.
Notes: The first of many “Murphy’s Laws” that come into play when discussing mishap investigations…

## Slide 40
Interviews

## Slide 41: Interviews
Review the Safety Investigator ISB Interview Guide found in the ISB Go Package prior to conducting any interviews
Ensure your ISB has copies of all the required interview forms
  Work with Wing/Safety or Delta/Safety to acquire all necessary interview forms, if necessary

## Slide 42: Interviews
Interviews can be privileged or non-privileged depending on the type of mishap
There are two parts to privilege:
  First, the deliberative process: The analysis of the evidence (witness statements, maintenance forms, training records, weather, etc.)
    This is a responsibility of the SIB, not that of the ISB
    The ISB gathers evidence, the SIB analyzes the evidence
  Second, statements taken under a promise of confidentiality
    ISBs are involved with the interview process
    As are SIBs
Notes: Interviews can be privileged or non-privileged depending on the type mishap
The next couple slides will explain the difference
Two parts to privilege (time for some lawyer speak)

## Slide 43: Interviews
When a promise of confidentiality IS authorized:
  For DAF nuclear surety, space, aviation, guided missile, directed energy, and friendly fire mishaps, or when authorized in accordance with paragraph DAF 91-204, Paragraph 4.5.2.1.
When a promise of confidentiality IS NOT authorized:
  For explosives, small arms, chemical agents, afloat, ground, motor vehicle, off-duty military mishaps, or incidents, or hazards, see DAF 91-204, Paragraph 4.5.2.1. for exceptions
Think privileged (promise of confidentiality) vs non-privileged interviews (no promise of confidentiality)
Notes: This is where ISBs are involved
Interviews with witnesses, mishap participants, etc.
Not all categories of mishaps have the option for the promise of confidentiality.
Think privileged (promise of confidentiality) vs non-privileged interviews (no promise of confidentiality)

## Slide 44: Interviews
Who IS authorized to make a promise of confidentiality?
  Members of a Safety Board
    ISB President, ISB Investigating Officer, SIB President, SIB Investigating Officer, or a single investigating officer (SIO)
    And only during safety investigations where promises of confidentiality are authorized
    When authorized by Board President or IO
    Who IS NOT authorized to make a promise of confidentiality?
    Commanders
    The safety office, unless appointed to safety board
Notes: Who can promise?
Not everyone is authorized to make promises of confidentiality
ISB and SIB Presidents & IOs – b/c they have training and in-depth understanding
Other members of boards can extend the offer on behalf of the President or IO
What if a pilot wants to tell his CC or DO what happened before being interviewed by ISB? Is information he provides to the CC/DO concerned privileged? No, they can’t offer the promise of confidentiality

## Slide 45: Interviews
Document the Promise
  How do we document the promise
    Use of non-privilege and privileged witness forms and statements
  Who could be offered a promise of confidentiality?
    Depends on circumstances of the mishap
      Mishap aircrew
      Maintenance
      Supervisors
Not all witnesses need or require a promise of confidentiality
Only make an offer of a promise of confidentiality if necessary
Notes: As stated on last slide: #1 INTERVIEW WEAK AREA ON ISBs
Not properly documenting what type interview is being accomplished (i.e., fails to read statement onto tape or have witness sign non-privileged interview form).
Problem for SIB if don’t annotate…SIB doesn’t know if they are looking at a privileged or non-privileged interview
Who can be offered will depend on the circumstances of the mishap
Pilot – almost always yes
MX – unknown until we know more about the mishap. If mx related mishap, most likely
ATC – If vectored pilot into side of mountain, yes. If just happened to be talking to at time of an engine failure, most likely no.
Farmer who witnessed the mishap - no
One way (Technique) to determine is by whether we think they might ultimately be found causal in a mishap
Or they have information and the only way they will talk is if promised confidentiality (knows about pilots altered FEF folder type thing)

## Slide 46: Interviews
ISB accomplishes initial interviews with:
  Mishap participants (Ops, MX) and eye-witnesses
ISB interviews are simple:
  “Tell me what happened” and let them talk uninterrupted
  Save any questions for the end
Leave detailed questioning for SIB
Don’t share information from other interviewees
  “In his interview, Capt Matthews mentioned …”
  This violates Privilege
Notes: ISB interviews are different then SIB interviews and should focus on documenting evidence, not determining cause.
Typical questions include:
“Tell me what happened” and let them talk uninterrupted. Jot down any questions and save them for the end of the interview
“What did you see/hear/smell/feel during….”
Area ISB most often gets wrong…

## Slide 47: Interviews
AF Portal / SIB Support
Notes: Where can the SIB find these forms?
SIB support documents found on the Air Force Portal site or in AFSAS under “SIB Go Package” or on AFSAS “Pubs and Refs” page in SIB and ISB Go Packages

## Slide 48: Interviews
Foot stompers!
  Be sure all interviews include the privilege or non-privileged statement
  Develop a list of who was interviewed and turn this list over to SIB
  “Tell me what happened….”
  For recorded interviews, let them tell their stories uninterrupted
  Make sure recording devices are adequate and functional
  Consider using two recorders
  Medical care always care takes precedence over interviews
Notes: ISB interview weak areas…
The ISB can make the SIB’s job easier by ensuring these interview items, as listed, are accomplished
Emphasize as “the weakest areas”
For recorded interviews let them tell their stories uninterrupted start to finish. If you have questions or want clarification save it until the end.
Be sure all interviews include the privilege or non-privileged statement found in SIB Support Package and the script is read on to the recorder BEFORE the interview begins

## Slide 49
Preliminary Reporting

## Slide 50: Preliminary Reporting
The Preliminary Message is fully releasable
  The first electronically transmitted safety message advising of a non-nuclear mishap
  Accomplished by IO, BP & Wing/Safety or Delta/Safety
  Will contain factual information only
  Will not contain safety-protected or privileged information
Although OPREP-3 reports do not satisfy this requirement, safety personnel should coordinate with the Command Post on OPREPs generated as a result of a mishap to ensure no inaccurate or privileged information is released
IAW DAFI 91-204, Table 9.1 Preliminary Messages are due within 1 day of the mishap occurrence
Notes: All safety mishap reporting is done via AFSAS, Air Force Safety Automated System
AFSAS is a CAC required system ensuring the protection of privileged information.
AFSAS can be accessed by safety officers and investigations boards to input and retrieve mishap data.
Classified mishaps are transmitted via the SPIRNET.

## Slide 51: Preliminary Reporting
Message Type and Responsible Party
  OPREP-3 (Command Post)
    “Just the facts”
  Preliminary Message (Safety / ISB)
    “Just the facts”
    1 day for aviation, ground, space, and weapons IAW AFI 91-204, Table 9.1
  Initial Public Affairs news release (PA)
    Fully releasable
    Facts from non-privileged sources
Notes: Following a mishap there are typically 3 different types of “reports”
OPREP-3 is a command post report
Safety Preliminary Report which is input into AFSAS. (explained on next slide)
  Typically done by the wing where the mishap occurred
  24 hours to release all categories
  It is a 100% factual report, fully releasable. Does not include any privileged safety information
    Info gathered from privileged witness interviews, speculation of why the mishap occurred, etc.
    We’ll look at a couple examples
PA news release

## Slide 52: Preliminary Reporting
What not to say in an OPREP-3 / Preliminary Report (Poor Example)
At 211805ZMAR15 Smith AFB CP was informed of an aircraft crash. Number of crew members is 1. The aircrew is active-duty Air Force crew assigned to the 7th Fighter Wing, 17th Fighter Squadron. Type of aircraft is an F-16C, tail number 85-0330. Aircraft was destroyed on impact. No collateral damage. Aircraft was on a local surface air attack training mission. Suspected cause of the mishap is engine failure. Interim Safety Board President is Col Harold, 7th OG/CD.
This example provides too much data – the OPREP needs to be a summary of the mishap
Notes: Not a good prelim
What information should not have been included?
Suspected cause of the mishap is engine failure.
Remember, just the facts.
QC before released. Make that step part of your IEMP 10-2

## Slide 53: Preliminary Reporting
What to say in an OPREP-3 / Prelim Report (Good Example)
Individual was found face down next to a B-5 maintenance stand by another maintenance member. He was unresponsive, emergency services were called. The county coroner declared him dead upon arrival.
Notes: Ground example – good
Just the facts, no privileged information is included

## Slide 54
SIB Arrival Preparation

## Slide 55: SIB Arrival Preparation
Lodging arrangements for SIB
Transportation requirements to / from mishap site
Determine work locations for SIB
On-Base / On-Site
Computer support
Communications support
See the SIB Go Package for the SIB Support Requirements List
Notes: These items should include…

## Slide 56: SIB Arrival Preparation
Notes: SIBs will need
Rooms to work in (3)
Projector to work daily activities logs
White boards to brainstorm on
Hangar space for wreckage, etc.
*Pics are from F-15 mishap Nellis Nov 12*
  Again, see SIB support package for SIB Support Requirements List

## Slide 57: SIB Arrival Preparation
Computer support
  One computer per SIB member
  High-capacity scanner
  Photo capable copier
SIB Drives
  Limited access shared drive on server
Stand alone computer for downloading
24 / 7 computer support
Back-up your working files daily!!!

## Slide 58: SIB Arrival
ISB members fill in and turn over all appropriate documents to their SIB counterparts during Changeover Briefing
Notes: Helpful technique: ISB BP checklist, each ISB member has a similar checklist, , good to fill in and ultimately turn over to SIB during the changeover to document ISB actions taken.
After the ISB handoff is complete the members are normally done and go back to their daily jobs. They may/can expect to receive calls from the SIB for more information on certain pieces of evidence.

## Slide 59: ISB Handover to SIB
Each SIB member should meet with their ISB counterpart to review gathered evidence
Ensure all Interview documentation is correct
ISB and SIB doctors discussing medical records
Notes: Following the briefing, the members of the ISB and SIB get together and exchange the data the ISB gathered.
Good time for ISB BP and SIB BP to identify support contacts (WG/SE, WG/CC, contracting officer, Incident CC, Security Forces, etc.).
Picture shows ISB and SIB flight doc exchanging data. There should be a one-on-one handoff between all the reps reviewing the checklists and inventorying the evidence, i.e., for a pilot all flight, evaluation and training records.
Have the IO and AFSEC rep review the interview doc for completion and accuracy to include 72-hr/7-day history

## Slide 60: Handover Points to Cover
Team Members
Mishap Data
Planned Mission and the Mishap Sequence
Status of Toxicology Testing and Witness Statements
Status of equipment involved in the mishap (launch or space vehicle, ground radar etc.)
Status of Records Impoundment
Media Interest
Logistics and Administration
Outstanding Issues
Local Area Safety
Notes: Areas to consider covering in the changeover briefing…..tailor to the type of mishap….don’t need status of aircraft for ground mishaps, weapons mishaps.

## Slide 61: Handover Points to Cover
Walk through mishap site
Update the Entry Access List (EAL) – removing ISB members and adding SIB members
When complete, ISB members return to their normal duties, but they need to be available in the short term if questions arise
Notes: Once the changeover is complete, if able have the ISB lead you on a walk through of the site.
Might not be convenient if wreckage is underwater or at the top of a 10,000’ peak.
Then take them off the EAL, they long longer have reason to access the site. If they need to go back out for any reason, they talk to you. There hava been cases where ISB members have decided to give tours after the handoff.
For example: T-38 Mishap Sheppard Jul 13. MA went into dense woods with lots of under brush. ISB knew where parts were, provided a walk through with the SIB President.

## Slide 62
Safety Investigation Board

## Slide 63: Purpose of the SIB
Determine the cause or causes of the mishap
Formulate recommendations to prevent future mishaps
Create three deliverables in AFSAS

## Slide 64: SIB Responsibilities
Responsibilities are covered in:
  DAFI 91-204, Paragraph 2.9. The SIB President or Investigating Officer
  DAFI 91-204, Paragraph 2.10. The SIB
  DAFMAN 91-222, Paragraph 2.6. Interim Safety Board President
  Local Wing or Delta Mishap Response Plan
Notes: ISB responsibilities are covered in DAFI 91-204.
Example shown is fictitious
Wing/Delta SE is OPR
Wing/Delta MRP has checklists for all ISB members and wing agencies and instructions on what to accomplish following a mishap

## Slide 65: Investigation Timeline
The SIB’s investigation timeline is listed in the table below:
DAFI 91-204, Safety Investigations and Reports

## Slide 66: Investigation Timeline
Investigations can be divided into 10-day periods
  Days 1-10 – Gather evidence, determine “what happened?”
  Days 11-20 – Analyze the evidence, determine “why it happened?”
  Days 21-30 – Write the report, prepare the brief for the Convening Authority, prep the final message for release in AFSAS - pending the Convening Authority’s approval
  Days 30-45 – Brief the Convening Authority
  Days 45-48 – Release the final message
Notes: Typical SIB timeline.
Our job finishes after the Convening Authority (MAJCOM Class A, NAF Class B) out briefing

## Slide 67: SIB Deliverables
Safety Report in AFSAS
Notes: 3 products the SIB will produce:
Safety report – Exhibits and data, which are entered into AFSAS, the AF’s computerized safety database
The briefing produced by the BP given to the convening authority at the conclusion of the investigation
The message report (mishap narrative, findings, causes, recommendations, etc.) which is also entered into AFSAS
Although work on each of these will be occurring throughout the SIB process, days 21-30 is when we’ll be finalizing these products

## Slide 68: SIB Deliverables
Brief to Convening Authority

## Slide 69: SIB Deliverables
Final Message

## Slide 70: Safety Investigation Guidance
DoD Guidance:
  DoDI 6055.07, Mishap Notification, Investigation Reporting, and Record Keeping
DAF Guidance:
  DAFI 91-204, Safety Investigations and Reports
Discipline-Specific Guidance:
  DAFMAN 91-221, Weapons Safety Investigations and Reports
  DAFMAN 91-222, Space Safety Investigations and Reports
  DAFMAN 91-223, Aviation Safety Investigations and Reports
  DAFMAN 91-224, Ground Safety Investigations and Reports

## Slide 71: Getting Started - Overview
Start a Filing System ASAP
  The ISB should have collected a large volume of paper and evidence
  If the ISB has not already filed this information, the SIB will need to do so
Filing Cabinets / File Plan
  Exhibits
  MX / Engineer Records
  Medical Records
  Personnel Records
File Inventory – Recorder
Electronic Filing System – SIB (Go) Package
  Use existing electronic folders
  Don’t make new / expand folders unless needed

## Slide 72: Getting Started - Overview
Start an Electronic Files Plan
One Folder For Each Exhibit
One Folder For Each SIB Member
Exhibits
Members

## Slide 73: AFSAS Accounts
All Primary SIB members need an AFSAS account
BP’s discretion whether Secondary members get AFSAS accounts or not
Start with Wing / Safety or Delta / Safety rep for help in establishing accounts, may have to contact the MAJCOM / Safety of FLDCOM / Safety to accelerate account and role approval
Make sure all members have elevated access and the proper roles
All members will use their accounts for entering their data in AFSAS
Download the SIB Go Package located in AFSAS for guidance and hos-to information

## Slide 74: Organize to Investigate
Review known circumstances of mishap with the ISB prior to hand-off and with the SIB after hand-off from the ISB
  Listen to ISB interviews as a group
  Review written interviews from ISB
  Set up a “re-interview” or “need to interview” list and schedule
  Review “products” received from ISB
Develop an office “game plan”
  Files, meeting schedule, what we know / what we think we know / what need to know, etc.
Develop a mishap site “game plan”
  Do you still need to observe, photograph, tag, and/or collect debris?
What technical assistance should be requested
  Do you need help from experts on certain pieces of equipment or systems?
Notes: Remember we need to get organized to investigate; we aren’t going to solve the mishap on day 1
Listen to the interviews the ISB conducted as a group
From the interviews get a feel for the “what” of the mishap and the mishap sequence
Take notes for follow up interviews
Based on what we’re hearing, what tech support does it look like we need be asking for
Determine if others need to be interviewed
Develop an office gameplan
Recorder developing and setting up file plan
Post sib phone #’s and address
Do we have all the support we need (computers, high speed scanner, a copy of Adobe Pro 9 for creating reports in a PDF format, shredder, printers, etc.)
Develop a crash site gameplan
Who needs to go out to the crash site (usually always MX member, possibly pilot member, not the IO (depends on circumstance of the mishap), needs to organizing the investigation)
What are we looking for in the wreckage
Begin to think about when we’re going to recover the wreckage and where are we going to put it
All SIB members names on EAL

## Slide 75
Safety Investigation Board Composition

## Slide 76: Board President
Colonel or higher
  For mishaps involving a fatality, the board president must be a brigadier general select or of a higher rank
  This rule applies to safety investigation boards (SIBs) and accident investigation boards (AIBs)
A graduate of the AFSEC Safety and Accident Investigation Board President Course (BPC) *required*
Equal to or greater in rank than the person involved
From outside the wing or delta which experienced the mishap

## Slide 77: Investigating Officer (IO)
Expertise in the area in which the mishap occurred in is not required
Manages investigation under direction of BP
  Directs and coordinates all phases of the investigation
  Runs daily meetings
  Coordinates timeline compliance with HQ AFSEC Rep
Writes majority of the Narrative
  Begin writing the narrative ASAP

## Slide 78: AFSEC Representative
Process expert
  Keeps SIB on the timeline
  Coordinates for technical assistance if/when needed
  Provides mishap investigation continuing education
Formal report “proprietor”

## Slide 79: Maintenance Expert
Maintenance procedures expert
Spacecraft history, maintenance procedures, training documentation
Directs wreckage recovery
Conduct interviews with maintenance personnel (within reason, per guidelines on interview techniques and recommendations)
Directs military technical support
Quality Assurance

## Slide 80: Primary Members
The following are conditional primary board members:
  Weather officer
  Weapons safety manager / EOD
  Etc.
Notes: A Conditional Primary Member is one you feel you need to add to the SIB or the convening authority adds based on the circumstances of the mishap.
In Primary status they can submit a minority report if they do not agree with the BP in the outcome of the investigation.
91-223 Table 5.4. If their area of expertise relates to a factor that was integrally involved in initiating or sustaining the mishap sequence, these individuals are required SIB members and are accorded Primary Member status. If the BP determines the conditional member’s area of expertise is not a factor in the mishap, this member serves as a secondary member.
For example, on the Dover C-5 SIB the SIB asked for a Loadmaster and Flight Engineer be added due to aircrew issues/factors in the mishap.
Any additional individual skill that you might need – ask for through the convening authority. They have to approve it, don’t just call one of your buddies and ask him/her to join the SIB.
Reference Chap 5 of AFMAN 91-223

## Slide 81: Recorder
Office manager and contracting office liaison
  Admin support / transcription supervisor
  Establishes and maintains filing system (start today!)
Tracks everyone associated with mishap and investigation
  Keeps a list of people (potentially) involved in the mishap
  Keeps a list of ISB members and SIB members
  Track who can and cannot have access to wreckage and/or other mishap information
  A secondary member
  Non-voting member
  Is the backbone of investigation!!

## Slide 82: Secondary Members
Administrative Specialists
Representatives of contract / test agencies if they participate on the board
Human Factors Consultant
Technical Experts
Notes: Other secondary members that could be added.
Again, will depend on the circumstances of the mishap
These are not voting members on the SIB.

## Slide 83
Interviews
(Privilege & Non-Privilege)

## Slide 84: Interviews
Privileged information is exempt by law from disclosure outside USAF / USSF Safety Channels, including:
  Testimony given to investigators (e.g., Witness Statements)
  Information obtained from contractors
  Investigation deliberative process (e.g., Findings, Recommendations, etc.)
  Reports and briefings produced by Safety Investigation Boards
Non-privileged information is “factual” information about a mishap (without analysis), including:
  Date and time
  Geographic or orbit location
  Equipment type
  Unedited pictures of the crash site
  Etc.

## Slide 85: Interviews
Protects the process by limiting access to SIB analysis
  No restaurant or bar talk!
  No talking to colleagues, friends, or family!
Have technical assistant reps and others outside the SIB sign the NDA, as appropriate for either contractors or military

## Slide 86: Interviews
Review the Safety Investigator SIB Interview Guide found in the SIB Go-Package prior to conducting any interviews
Ensure your SIB has copies of all the required interview forms.

## Slide 87: Interviews
Who can offer Privilege?
  Designated ISB members
  Designated SIB members
  Single Investigating Officers
Who should privilege be offered to?
  Depends on circumstances of the mishap
    Mishap aircrew
    Crew chief
    Maintenance
    Launch or orbit experts
    Supervisors
Not all witnesses need / require promise of confidentiality

## Slide 88: Witness Interviews
Who should conduct the interviews?
Someone who is:
  Same gender, rank, and / or of the same job description
  A people person
  An “area” expert
  Who is available
  If two are sent -- only one conducts the interview
Don’t allow “observers” to sit in on the interview
Non-interviewers can listen to interview recordings after the fact, if necessary and under appropriate circumstances
Notes: Who would you pick?
The area expert.
Keep the interviewing crowd to a minimum to keep from intimidating the witness
One on one is best
If two accomplish the interview, not a good cop/bad cop scenario
BP does interviews at the senior staff level
Witness can be compelled to meet with interviewer by CC/Shirt, but not what to say.
Privilege prevents self-incrimination (no adverse administrative action / not releasable outside Safety channels)
Consider ending questions…
What do you think caused the mishap?
Is there anything I didn’t ask that you would like to add?

## Slide 89: Witness Interviews
Witness name and date on each recorded file
  Privileged or non-privileged interview
Establish a polite & professional rapport
  It is not an interrogation
Let them talk
  Do not interrupt a witness while they are narrating an event
Question in a logical sequence
  Don’t lead the witness
Don’t argue / disagree / disapprove
If a witness provides a statement under medication, add a notation to their statement
Don’t let witness question you
Notes: All are important
Read each bullet

## Slide 90: Witness Interviews
Interviews typically go from general questioning to specifics
  From “Tell me what happened …”
  To “Which checklist did you follow and why …”
  3 to 6 (multiple) interviews with mishap participants / observers
  Take notes to highlight details for further questioning or investigation

## Slide 91: Release of Information
Who can a SIB release information to?
  The SIB can release information to:
    The Convening Authority
    *You are working for the Convening Authority
    Convening Authority Safety Staff
    AFSEC
  The SIB cannot release information to:
    Rest of the Convening Authority staff
    What about
      Mishap Wing / Commanders or
      Mishap Delta / Commanders???
    NO!
Notes: We work for the 4 star directly so we can release info to him? To the 2-star MX/CC?
-No, ask approval of 4-star first
MAJCOM safety staff
-Yes, we are working with them to complete the investigation and they understand not to release information
Release info to HQ AFSEC?
-Yes, we are working with them to complete the investigation, tech support issues, etc.
Wing cc or wing safety staff?
-No, unless they are the convening authority, why not?
-All others are specifically excluded from the flow of information in order to prevent opportunities for other commanders to unduly influence the SIB investigation and findings. The appropriate avenue for wing commanders to request information from a SIB is through the convening authority.

## Slide 92: Release of Information
What if???
Investigators discover information which seriously impacts the operation of a weapon system.
  Immediately notify the Convening Authority and, potentially, the unit commander
  Regardless of whether such information is associated with the mishap currently under investigation or not
  The convening authority will notify other action agencies, the appropriate program manager for the weapon system or other items involved, the weapons system lead command, and HQ AFSEC
  These action agencies must evaluate the nature and seriousness of the information, determine the proper response, and issue required instructions
Notes: This is the process.
Contact the convening authority safety office and relay the information.
Let them determine the next step, then get back to investigating
If a SIB discovers information that seriously impacts the safe operation of a weapons system, they must immediately notify the Convening Authority, and potentially the unit commander if the Convening Authority notification cannot be made in a timely manner, regardless of whether such information is associated with the mishap currently under investigation.

## Slide 93: Technical Support
Tech assist ROE:
Requested by SIB through HQ AFSEC
  Mishap Board Technical Assistance / DSN 246-5867 / Commercial 505-846-5867
Do not directly contact contractors or vendors for teardown and analysis without speaking to the System Manager or HQ AFSEC first
  Normally reps are paid by the SPO under contract
  Outside lab and/or specialists may need a contractual vehicle prior to providing any technical assistance
Notes: For technical assistance, if requested by the SIB.
Do not directly contact contractors or vendors for teardown and analysis without speaking to the System Manager or HQ AFSEC/SES first.

## Slide 94: Technical Support
There are two general types of technical support
Support from:
  The manufacturer / contractor that designed, built, or maintained the equipment (like GE, Lockheed Martin, etc.)
  DOD military / civilian personnel (like ALCs, SPO, Depot, AF Labs)
The distinction is important!
  The difference will determine how to go about requesting technical assistance and who is authorized to initiate the request
Notes: Another form of Technical Support is the MAAF located at AFSEC.
For flight mishaps the MAAF is your source for downloading FDRs/CVRs
The MAAF will produce your animations if you need one.
Contact the MAAF through the technical assistance hotline as shown on previous slide - DSN 246-5867 Commercial 505-846-5867

## Slide 95: MAAF
Mishap Analysis and Animation Facility (MAAF)
  Air Force focal point for recovery of data from flight data recorders (FDR) and cockpit voice recorders (CVR) for USAF safety investigations per DAFI 91-204
  Contact the MAAF through the technical assistance hotline
  MAAF has organic capability to recover data from damaged recorders
  MAAF produces plots, tabular listings, copies of CVR and animations
Is this slide needed for space mishaps?

## Slide 96
Narrative

## Slide 97: Preparing the Narrative
The non-privileged exhibits or documents make up Part 1 of the report
They are considered “factual”
These various exhibits contain copies of:
  Maintenance records
  Photos of the crash site and a crash site diagram
  Non-privileged witness interviews
  Space weather, if applicable
  Etc.
At the conclusion of the SIB, these exhibits are turned over to an AIB, if an AIB convenes
  “If witnesses provide statements without a promise of confidentiality, the interviewer will inform the witness that their statement will be provided to the Accident Investigation Board (if applicable) or other legal investigations and/or may be releasable to the public pursuant to a FOIA request.” (DAFI 91-204, Paragraph 4.5.5.)
Notes: Narrative is the report produced by the SIB documenting why the mishap occurred, findings, causes and recommendations.
The “tin kicking” portion of the SIB is over and it’s time to put pen to paper
Writing on this should have started in the days 11-20 period.
Length of the report will depend on the circumstance of the mishap, there is no set length.
* Reformatting in AFSAS required. Personal information, HIPA, proprietary information, etc. removed.

## Slide 98: Preparing the Narrative
The privileged exhibits or documents make up Part 2 of the report
They are considered “factual”
These various exhibits contain copies of:
  Maps and charts
  Technical and engineering reports
  Testimony and witness statements
  Etc.
Most privileged safety information “must not be revealed to any other investigation or used to support any legal proceedings or punitive actions resulting from the mishap.” (DAFI 91-204, Paragraph 4.8.3.4.)
Notes: Narrative is the report produced by the SIB documenting why the mishap occurred, findings, causes and recommendations.
The “tin kicking” portion of the SIB is over and it’s time to put pen to paper
Writing on this should have started in the days 11-20 period.
Length of the report will depend on the circumstance of the mishap, there is no set length.
*Reformatting in AFSAS required. Personal information, HIPA, proprietary information, etc. removed.

## Slide 99: Preparing the Narrative
The post-investigative exhibits or documents make up Part 3 of the report
They are considered “factual”
These various exhibits contain copies of:
  Investigation briefing
  Additional files, if available
These have the potential to be released to an AIB, but only if certain approval is granted – see the topic of Authorized Use and Release of Privileged Safety Reports and Information in DAFI 91-204 for further information
Notes: Narrative is the report produced by the SIB documenting why the mishap occurred, findings, causes and recommendations.
The “tin kicking” portion of the SIB is over and it’s time to put pen to paper
Writing on this should have started in the days 11-20 period.
Length of the report will depend on the circumstance of the mishap, there is no set length.
* Reformatting in AFSAS required. Personal information, HIPA, proprietary information, etc. removed.

## Slide 100: Preparing the Safety Report
Notes: AFSAS is where we’ll input our exhibits, some are optional, some are required based on type/class of mishap.
Point out column

## Slide 101: Narrative
Most time consuming, least enjoyable phase
The Narrative is heart and soul of the SIB process
Factors / Findings / Recommendations are core of the Narrative
  Expect between 15,000 to 20,000 words in length
  30 to 60 pages
Becomes the final message report
Notes: Narrative is the report produced by the SIB documenting why the mishap occurred, findings, causes and recommendations.
The “tin kicking” portion of the SIB is over and it’s time to put pen to paper
Writing on this should have started in the days 11-20 period.
Length of the report will depend on the circumstance of the mishap, there is no set length.
* Reformatting in AFSAS required. Personal information, HIPA, proprietary information, etc. removed.

## Slide 102: Narrative Data Sources
Narrative
Interviews
Technical Teardowns
Training Records
Tech Orders
Risk Management
Asset Recorders
Notes: What Sources of data to compile for Narrative

## Slide 103: Preparing the Narrative
See applicable regulations for guidance on preparing the narrative
A process that is more of an “art” than a “science”
Narrative template / example provided in SIB Go Package
Review the format and writing style
Responsibility of all SIB members to draft, but the IO typically compiles content
Notes: Guidance for the reports can be found in the applicable AFMANs
All SIB members will write their applicable section, IO’s job to compile
Problem with this is it becomes a document by committee with different writing styles.
Up front get folks to agree on certain writing ROE - will make IO’s job easier
Come to consensus on what to call individuals involved in the mishap (MP, MC, MM1, W1 etc..)

## Slide 104: What to Why
The investigation needs to be done in a sequential and consistent manner, so all relevant facts are collected before any conclusions are drawn
DO NOT CONCENTRATE ON ANY ONE AREA TOO EARLY IN THE INVESTIGATION TO THE EXCLUSION OF OTHER AREAS
Notes: Several other keys during this period.
Emphasize… Ensure The Facts Lead To The Conclusion, Rather Than The Other Way Around!
Don’t take your day 1, walking in the door, based on what I know about the mishap theory and try to make the facts fit it (inexperienced investigators do this too)
Keep asking why.

## Slide 105: What to Why
Without finding the “Why,” the failure will occur over and over
Keep asking “Why” until reaching a dead end
Elevator fell off … Why?
Bolt failed ... Why?
Improperly installed ... Why?
T.O. wrong ... Why?
Not field tested ... Why?
No requirement to field test … Bingo!
Notes: The key here is to keep asking why.
Start with the last event in the mishap sequence and work backwards, keep asking why.
The unanswered “whys” is where the investigation focus needs to be.
For example:
Note: The line represents where most inexperienced investigators stop.
There Is A Temptation to Grasp at First Plausible “Why,” Cease Investigating and Start Writing
Recommendations to fix the bolts will not keep this mishap from happening again.
We need to get to the root cause; the bolt failure is not the root cause.

## Slide 106: Preparing the Narrative
Sequence of Event
Investigation Conclusions
Background Information (Person, Object, General)
Factors (Factors, Causal Factors, Non-Factor Worthy of Discussion)
Primary Findings
Primary Recommendations
Other Finding of Significance, Other Recommendation of Significance (OFS / ORS)
Glossary of Terms and Acronyms
Referenced AFSAS Reports
Notes: This is how things will appear in the final message but not how it’s organized in AFSAS
Investigation conclusions will be written last
Each of these areas are data field inputs

## Slide 107: Prepare the Report / Write the Narrative
Objective is to show
  Areas investigated
  Factors accepted with rationale
  Potentially relevant factors considered and rejected, with rationale
Use illustrations to clarify if required
  A picture is worth a thousand words
Notes: It is important to remember to not only include what was ruled in and why with regards to being a factor in the mishap sequence, but what was ruled out and why. Explain the process used to arrive at the conclusions. If an issue could have “reasonably” been a factor in the mishap sequence but wasn’t, explain in the appropriate section how the SIB determined it wasn’t a factor. Not all non-factors need to be discussed. For example, if the SIB is dealing with a gear-up landing and during the course of the investigation determined that airfield NOTAMs were not an issue, that doesn’t warrant mention in the report. However, given the same gear-up landing, if the SIB determined that recent maintenance performed on the landing gear wasn’t a factor, that deserves discussion on how it was ruled out.
The use of illustrations can help to clarify SIB discussions

## Slide 108
Mishap Factors

## Slide 109: Factors
Factor: unusual, out-of-the-ordinary, or deficient action or condition discovered in the course of a mishap investigation that contributed to the eventual outcome
  Most mishaps involve multiple factors
  Examples of factors:
  Supervision
  Qualifications
  Weather
  Logistics
  Maintenance
  Mission Planning
  Discipline and Execution
  Currency / Experience
Notes: First, we need to determine the “factors” in the mishap.
A factor is - read the definition
Factors: Enable the investigator to take the investigation from everything is on the table to these are the areas that are significant

## Slide 110: Factors
Trainer aircraft has an unrecoverable in-flight engine shutdown when the Instructor Pilot (IP) inadvertently pulls the throttle to cutoff at low altitude while reducing the power to idle. Poor throttle finger lift design allowed the possibility of inadvertent shutdown of engine. After ejection, the pilot was unable to contact search and rescue due to survival radio battery failure.
  T.O.s fail to address the possibility of inadvertently cutting of the engine when using the throttle
  “AIRCRAFT DESIGN” – Throttle finger lift design allowed possibility of inadvertent shutdown of engine
*Flight Mishap Example

## Slide 111: Factors
The pilot rushed his preflight due to extremely cold weather and failed to notice an engine cowling was left unlatched by maintenance personnel. The engine cowling opened during takeoff and damaged the leading edge of the wing.
  “Pilot Actions” – Pilot allowed his preflight to be rushed
  “Weather” – Cold weather caused the pilot to rush his preflight
  “Maintainer Actions” – MX failed to properly latch the cowling
*Flight Mishap Example

## Slide 112: Factors
Non-Factors Worthy of Discussion: Factors discovered as potentially causing this or another mishap but did not influence this mishap
  Possible factors in the investigation that we ruled out (i.e., bird strike in an engine failure mishap)
  Things we uncover during the investigation that did not cause the mishap or influence the outcome but that we want to have fixed due to the potential to be a factor in a future mishap (i.e., failure of survival radio batteries)
  Commander interest items (like Risk Management (RM), Cockpit Resource Management (CRM)), etc.
*Flight Mishap Example
Notes: Non-Factors Worthy of Discussion could fall into one of three categories:
Possible factors in the investigation that we ruled out (i.e., bird strike in an engine failure mishap)
Things we uncover during the investigation that did not cause the mishap or influence the outcome but that we want to have fixed due to the potential to be a factor in a future mishap (i.e., failure of survival radio batteries)
Commander interest items (like RM, CRM, etc.)

## Slide 113: Factors
Explain why causes, such as human error, supervision, or equipment failure occurred
Factors are not mutually exclusive
Most mishap involve multiple factors
Factors explain the Findings in detail

## Slide 114: Factors
Integral to a good investigation
Identified as part of the investigative process
Factors are written in order of precedence (most to least important in relation to your mishap)
Factors are grouped by causal factors, Factors and Non-Factors Worthy of Discussion
Until we know mishap factors:
  Cannot write the Narrative
  Cannot create Findings and Recommendations

## Slide 115: Writing
Factor Title (e.g., “Technical Data Compliance”)
Analysis: SIB method to determine the factor’s influence on the mishap scenario
  Include enough information so the reader can logically follow the SIB’s rationale for conclusions reached
  Should include references, as appropriate, to specific Technical Orders/Publications, training received, actions accomplished, results of technical analysis, etc.
Determination (Factor, Causal Factor, Non-Factor Worthy of Discussion)
Notes: The format for writing the paragraphs in the Narrative
Emphasis Bullet:
Recurring weak area: Include enough information so the reader can logically follow the SIB’s rationale for conclusions reached.
SIBs do a great job explaining the “what” in the mishap sequence, often come up short in explaining “why”
SIBs have problems with this, show you how to overcome in a few slides

## Slide 116: Writing
Factor Title (e.g., “Technical Data Compliance”)
Analysis: SIB method to determine the factor’s influence on the mishap scenario
Often it is helpful to organize this section into a discussion:
  How the particular action should have been accomplished
  How it actually occurred during the mishap
  Why the difference
  How this contributed to the mishap
The last portion of each factor analysis will be a brief summary that ties the discussion together
Notes: Emphasis Bullet:
Recurring weak area:
What should have happened/what’s the standard
What actually happened
How it contributed to the mishap and why the difference
Close with a tie-it-all-together statement
This analysis format makes the logic easy to follow and for the reader to come to the same conclusion

## Slide 117: Writing
Problem Areas:
Where Did You Get The Information?
  Smith AFB now checks torque in accordance with T.O. procedures during the 300-hour phase inspection
  What is the T.O. reference for this torque check?
  The SIB examined documentation of widget pin removal and reinstallation in the AFTO 781As.
  The investigation revealed the mishap aircraft (MA) was towed four times yet had no AFTO 781A documentation for pin removal / reinstallation.
  Where does it say this is required? IAW with which T.O. and which paragraph #?
  If you’re going to say they’re not following guidance, be sure to give the references to the guidance document(s) that is (are) not being followed
Notes: Another weak area. Where did you get the information?

## Slide 118: Findings
FACTORS
FINDINGS
RECOMMENDATIONS

## Slide 119
Mishap Findings

## Slide 120: Findings
Statements in chronological order of each single event or condition essential in sustaining the mishap sequence
Findings represent the SIB's conclusions after analyzing and deliberating all the facts
Technique: Bullet overview of the mishap (in complete sentences) in chronological order from the first event in the sequence to the end of the mishap sequence
  Represent the “factors” in the mishap
  Represent the events that sustain the mishap sequence
Notes: What are findings as defined in DAFI 91-204?
Technique: Bulletized (but in complete sentences) mishap overview in chronological order from the first event to the end of the mishap sequence
There are two types of findings:
The “factors” in the mishap
The events that sustain the mishap sequence

## Slide 121: Findings
List findings in time sequence, first to last
  When it occurred, not when discovered
  Design / T.O.s / Regulations / Training / Mishap
  Some event sequences begin long before the actual mishap sequence with design problems, improperly written directives, or inadequate training programs:
    Finding 1: The F-117 basic aircraft design is highly conducive to spatial disorientation.
    Finding 1: A known design deficiency in the KC-135 engines predisposes the third stage fan disk lugs to fractures due to high cycle fatigue (HCF).
The last finding ends with all damage / injury.
*Flight Mishap Example
Notes: As further defined in the 91-204 paragraph 5.10
After reading it is still tough to determine what exactly findings are/look like unless you’ve worked with them previously.
Emphasis Bullets
List findings in the order of when they occurred relative to the mishap sequence, not when discovered by the SIB
Some Event Sequences Begin Long Before the Actual Mishap Sequence With Design Problems, Improperly Written Directives, or Inadequate Training Program:
Finding 1: The F-117 Basic Aircraft Design Is Highly Conducive to Spatial Disorientation (SIB written Finding 1 following an F-117 SD mishap).
Finding 1: A Known Design Deficiency in the FXXX Engines Predisposes the Third Stage Fan Disk Lugs to Fractures Due to High Cycle Fatigue (HCF)

## Slide 122: Findings
When event cannot be supported by facts, come up with reasonable measure of probability based on evidence, professional knowledge, and judgment.
For example:
  Finding XX: The mishap pilot failed to recognize a continuous shallow descent, most likely due to a combination of the following reasons:
    Channelized attention
    Cognitive task oversaturation
    Incorrect instrument-crosscheck
*Flight Mishap Example
Notes: Despite your best efforts, often times you won’t know with 100% certainty why a mishap occurred
You’ll have a reasonable idea based on the evidence gathered and analyzed, but
For example: a fatal mishap where the key witness can’t be interviewed to determine why they took the course of action they did.
In that case, we qualify the findings with words like “most likely” or “for an undetermined reason”
Take the term “most likely” out of the sentence above and how does it read?

## Slide 123: Findings
Before the first Findings session:
  Ask IO or AFSEC rep to draft initial set of findings based on discussions to date
As a rule of thumb, expect between 8-15 findings
If you've got more findings than that (typically, SIBs initially have too many findings) it's likely some findings can be combined or deleted
Don’t confuse mishap severity with the number of findings required
Notes: Have the IO draft an initial set of findings based on the circumstances of the mishap and post them on the board prior to the first findings session.
8 -15 findings is a good ballpark for the number findings, some will have more, some less.
The findings should be reviewed everyday by the SIB, as a group, until they are finalized.

## Slide 124
Causes

## Slide 125: Causes
Causes are those factors / findings that singularly or in combination with other causes resulted in the damage or injury
According to DAFI 91-204, Cause is defined as:
  … is a deficiency, which if corrected, eliminated, or avoided, would likely have prevented or mitigated the event damage or injury. In most instances a causal deficiency is correctable by commanders, supervisors, or individuals.
According to DAFI 91-204, Causal Findings are defined as:
  … are deficiencies in the mishap sequence, which if corrected, eliminated, or avoided, would likely have prevented or mitigated the damage or injury.
Mishaps can have multiple causal factors and findings
The intent of identifying causal parties in an investigation is to identify the point where corrective action is needed, not to place blame
Notes: After we determine the findings, we need to decide where cause fits in the sequence…which findings are causal.

## Slide 126: Causes
Findings which sustained the mishap sequence, but were normal to the situation (i.e., Expected Result), are not causal
For example …
  An engine failure occurring after a fuel boost pump failure is an Expected Result and not causal
CAUSE and EFFECT relationship
  Cause = “Why” it happened
  Effect = “What” happened
Pilot over-Gs aircraft, wings depart
  Cause = Pilot over-G
  Effect = Wings departing
*Flight Mishap Example

## Slide 127: Causes
Apply the reasonable person, reasonable publication, reasonable part concept when determining a cause
  If performance or judgment was reasonable considering the circumstances, do not assign cause
  If personal action was “reasonable” based on training received or published guidance, that action can not be causal, although deficient training or guidance might be
  Refer to DAFI 91-204, Paragraph 8.6.1. for more information
Notes: Be sure to look at “reasonableness” when determining cause.
Reasonable Person, Publications, Parts
This is very subjective. What is reasonable to you might not be to the rest of the SIB.
For example, let's say we’ve had 8 Class A F-16 nozzle loss mishaps. First one occurred 7 years ago. Dash-1 still contains nothing about how to fly the aircraft minus the augmenter nozzle. Is this reasonable?
After the first mishap, it probably would be reasonable because we would never expect the augmenter to fall off the aircraft.
Seven years, and 8 Class A mishaps later is it still reasonable?

## Slide 128: Findings Example
The Scenario: An F-15 was on a red X for a hydraulic leak which required maintenance to replace the number one hydraulic gear box. During maintenance just prior to the mishap flight, a B-nut to the number one hydraulic gear box input side was under torqued because of ambiguous wording in the T.O.XXX, X.X.X. The T.O. does not present a specific torque setting but simply states “tighten two turns after hand tight is achieved.”
The aircraft took off, on departure the pilot got a number one engine fire light due to hydraulic fluid leaking from the under torqued B-Nut igniting in the engine bay. The pilot properly shutdown the engine IAW T.O. 1F-15A-1, declared an emergency and initiated an emergency return to the airfield.
*Flight Mishap Example
Notes: Tell audience to read this and the following slide and we’ll demonstrate how it was used to build a set of findings

## Slide 129: Findings Example
On approximately a one mile final, tower called the pilot and requested the number of souls on board and fuel remaining. While answering the radio call the pilot allowed the aircraft to get slow which resulted in a high sink rate. The aircraft touched down in the overrun and the left main gear collapsed due to overload from the excessive sink rate which exceeded the design limited of the gear. With the left main landing gear collapsed the aircraft departed the left side of the runway approximately 1000 ft. past the overrun and sustained Class A damage to the left wing. The pilot egressed uneventfully.
*Flight Mishap Example

## Slide 130: The Scenario – Factors / Findings
What are the possible Factors in the mishap?
What are the possible Findings in the mishap?

## Slide 131: The Scenario – Factors
T.O. Guidance
Mishap Pilot’s (MP’s) Approach

## Slide 132
Recommendations

## Slide 133: Recommendations
Recommendations are feasible and effective solutions to eliminate identified hazards, or if the hazard cannot be eliminated, to mitigate the hazard’s potential consequences
Recommendations should target one or more of the hazards identified and documented during the investigation
All mishap investigations should include recommendations to prevent future mishaps
Notes: Next, we’ll determine the recommendations aimed at preventing future mishaps.
Recommendations are defined as…………..(read slide)
Recommendations must relate to the findings, causal or not causal, in the mishap sequence.

## Slide 134: Developing Recommendations
Technique
    What are you trying to get the recommendations to accomplish? List that before starting to finalize the recommendation wording
    Look at like recommendations in AFSAS. How were they worded?
Notes: What are you are you trying to get the recommendations to accomplish? List that before starting to finalize the recommendation wording. Blue sentence above the recommendations listed beneath.
If you get stuck on how to word a recommendation look at like recommendations in AFSAS. How were they worded?

## Slide 135: Developing Recommendations
To eliminate or mitigate the identified hazards consider the following
  Design (Implement a fixed gear)
  Incorporate Safety Devices (Implement an auto-extend system)
  Provide Warning Devices (Implement cockpit warning lights)
  Develop Training and Procedures (Improve the checklist or its use via training with instructors and in simulators. Ex: Mandate use of personal protective equipment.)
Notes: Consider the four methods listed for developing recommendations.
From top to bottom; design – longest timeline, normally most effective, most expensive;
Develop training procedure – least effective shortest time
May recommend long term design recs and other interim recs for mitigation until the hazard is designed out

## Slide 136: Developing Recommendations
The scenario and Possible Recommendations:
  Fix the ambiguity in the T.O.
  Require the B-nut be safety wired
Notes: These are the recommendations that would have come from the depot findings/causes example we built……………..
Avoid making do your job recs.

## Slide 137: Developing Recommendations
Recommendations should require the action agency to correct a deficiency rather than to implement a particular solution
  Poor: Move the right engine fire shutoff switch to the right side of the cockpit
  Better: Implement changes to the engine fire push-buttons to help preclude engine shutdown errors
Recommendations should be “closable”
  Conduct refresher training of all depot maintenance personnel emphasizing proper tool control procedures.
  Train contractor technicians to utilize data logger information in troubleshooting in-flight problems.
Notes: Recommendations ROE as found in DAFI 91-204
The action agency normally has greater expertise than the investigators and should be given the opportunity to develop the optimal solution for a problem.
In most cases, it is not necessary to recommend a study or evaluation, since studies or evaluations are implicit in the process.
Again, for a complete listing of recommendations ROE see 91-204 para 5.12.
Review 91-204 after writing recommendations to ensure they are valid
Others include:
- General, vague, sweeping, or open-ended recommendations that cannot be closed by the action agency are not appropriate. Write recommendations that have a definitive closing action.
- Do not recommend briefing personnel on the mishap. Such a briefing is a basic commander responsibility and a normal function of safety offices at all levels of command.
Do not recommend reminding (or CC’s reminding/briefing/publishing an FCIF to remind) personnel of the importance of simply doing their jobs properly.
  However, recommendations to place CAUTIONS and WARNINGS in TOs guidance relating the adverse consequences of not doing one’s job properly may be appropriate.
  Recommendations for specific action such as refresher training, implementing in-process inspections, etc., to ensure job duties are being properly performed, may also be appropriate since they are specific and can be closed.
  Closeable BULLET ONE AND TWO: IS THIS ONE TIME TRAINING OR ANNUAL? IF ANNUAL HOW CLOSE (WRITE INTO GUIDANCE AS ANNUAL REQUIREMENT)

## Slide 138: Developing Recommendations
Make sure recommendations wording can stand alone to be understood
  Perform a One-Time inspection (OTI) on the remaining aircraft in the B-1 fleet.
  Inspection of which component or system specifically?
Notes: This recommendation related to other recommendations made for the same mishap, but if the other recommendations aren’t reviewed at the same time, what does this mean?

## Slide 139: Recommendations - OPRs
OPR (Office of Primary Responsibility)
  If a recommendation requires funding to effect changes, assign to the appropriate office within the lead command as OPR
  OCR (Office of Collateral Responsibility)
  If another organization is responsible for performing or managing the work, assign these organizations as OCRs
  Recommendation X: Implement changes to the F-16 brake system to reduce the probability of encountering “hot brake” temperatures.
  OPR: ACC/A8
    ACC/A8 is responsible to arranging the funding
  OCR: AFLCMC/LAB
    AFLCMC/LAB would either perform the required work or would manage the contracted effort
Notes: One of our major challenges when writing recommendations is to identify the OPR who will be tasked to execute the recommendation.
Some actions can be taken at unit level. Other recommendations require MAJCOM or other agency actions
Basic ROE…………..(see slide)
If funding is involved, it usually comes back to lead command for the MWS.
ACC is the lead command for the F-16, not PACAF or ANG
ACC would be the OPR for F-16 modifications.
Some recommendations are handled at the unit level.
Reducing the bird strike hazard at base X following a bird strike Class A mishap would usually fall to the local unit (fix the drainage ditches where birds gather, etc.)
Non AF OPRS: Sometimes the responsibility for a recommendation lies outside the Air Force (e.g., the FAA for various air traffic control issues). Since the Air Force may not have the authority to task such agencies to perform recommended actions, do not assign non-Air Force agencies as OPRs or OCRs. In these cases, write the recommendation as an Air Force action and assign the appropriate Air Force organization as OPR. This Air Force organization is typically responsible for interaction with or contractual oversight of the outside agency and will ensure proper recommendation evaluation and disposition. Assign OCRs as required.
Emphasize
SIB/SIO is responsible for coordinating all recommendations with their proposed action agencies (OPR and OCR).
Ensure the correct OPR and OCR(s) are identified through positive contact (call or email them) prior to publishing the formal report or final message.
Include the office symbol, commercial telephone number, and email address of one OPR action officer for each recommendation. Place this information in the dedicated data field provided by AFSAS.
Contact the convening authority safety office to ensure proper action agencies have been identified.

## Slide 140: Recommendations
Recommendations aimed at preventing mishaps are the reason the SIB is convened
They are most important outcome of the investigation
Take the necessary time to get each recommendation correct
Notes: Recommendations will prevent future mishaps.

## Slide 141: Summary
SIB Techniques Guide can be found in the SIB Support Go Package, located in:
  Air Force Portal
  AFSAS
This SIB Support Guide covers the information we just covered in a narrative format broken out chronologically and by members’ duties.
This is an excellent read for all members of the SIB once you arrive on-scene

## Slide 142: Questions?