## Slide 1: Safety Investigation Board SIB Briefings
AFSEC/SEFF
1 Aug 2023

## Slide 2: How to use this presentation
This Slide Deck Contains Two Briefings
“SIB Day One” Brief SIB Days 1-10 Actions
  Days 1-10 actions are a planning estimate for gathering info to determine “what” happened and may require more or less time.
    This presentation is intended to be an intro/refresher to the USAF safety mishap investigation process. It details a lot of the actions the SIB should be focusing on during this time period, both investigatory and administrative.
    There is no need to go through the entire presentation on day 1. Stop at a logical point for your SIB, and resume at a later date when appropriate (For example, a common “best-practice” is to wait a few days before covering the factors section to avoid focusing the team’s attention on the “why” too early in the investigation.)
Notes: DAFMAN 91-223, Aviation Safety Investigations and Reports: 6.3. SIB Day One Briefing. After the ISB handover briefing, the SIB IO or AFSEC Representative will provide the “SIB Day One” briefing to the SIB members. (T-2) The briefing provides an overview of SIB member roles and responsibilities, investigation process, and reporting timelines. The SIB IO or AFSEC Representative should ensure SIB primary members review their associated checklists located in the SIB Go Package.

## Slide 3: How to use this presentation
“SIB Report Writing Briefing”
  This presentation covers many of the aspects of writing and exhibits for the SIB.
    This is the last part of the investigations process, but writing can still begin during the initial phase when determining what happened and why it happened

## Slide 4: Safety Investigation Board “Day One” Brief (Days 1-10)
AFSEC/SEFF
1 Aug 2023

## Slide 5: Mishap Investigation Guidance
Overarching Air Force Guidance
  DAFI 91-204 - SAFETY INVESTIGATIONS AND REPORTS
Discipline Specific Guidance
  DAFMAN 91-223 - AVIATION SAFETY INVESTIGATIONS AND REPORTS
  MAJCOM Supplements where applicable
Notes: Here is the guidance we’ll be using………Recorder/AFSEC Rep will download and post most current versions from ePublishing website.
Failure to reference will result in an incomplete report and likely return during CA and/or AFSEC Quality Control Reviews

## Slide 6: Purpose of the SIB
Determine the cause or causes of the mishap and formulate Recommendations to prevent future mishaps
Notes: The reason for mishap investigations is to try to make sure the same thing doesn’t happen again. We’re not here to blame anybody, but we do need to figure out the bottom line cause of the mishap to make recommendations to keep it from happening again.
DAFI 91-204, Safety Investigations and Reports: 8.1. SIB Duties. SIBs will ensure all on-duty safety investigations culminate with a safety report that contains a narrative sufficient for conveying mishap prevention information to the reader. The safety report contains the investigation, analysis, conclusions, and recommendations of the SIB. The SIB will write the safety report so the reader clearly understands how the findings and causes were determined and clearly states the role of the individuals found causal in the event sequence.

## Slide 7: How Do Investigations Prevent Mishaps?
Recommendations…..the Single Most Important Result of a Safety Investigation
Address Mishap Causes (Causal Findings)
Determining Accurate Root Causes = Mishap Preventing Recommendations
Notes: Determining Root Causes will lead to mishap preventing Recommendations.
DAFI 91-204: 8.9. Determining and Documenting Recommendations. Safety reports include recommendations that are feasible and effective solutions to eliminate identified hazards, or if the hazard cannot be eliminated, to mitigate the hazard’s potential consequences. SIBs will ensure recommendations correspond to one or more findings.

## Slide 8: Types of Investigations
Safety Investigation Board (SIB)
Conducted to find cause(s) of mishaps to take preventative actions
Recommendations to prevent future occurrence
Not Releasable
vs.
Accident Investigation Board (AIB)
  Conducted for all other Purposes including Claims, Disciplinary, Administrative Actions, etc.
  Statement of Opinion on Cause(s)
  No Recommendations
  Fully Releasable
Notes: To set the stage, there are two types of investigations following a Class A mishap, convened for two different reasons………………
We’ll be involved In the SIB process…..
DAFI 91-204: 1.1. Purpose of Investigations and Reports. Safety investigations are conducted, and safety reports are written, to prevent future mishaps. Legal investigations and boards are conducted for all other purposes. Commanders may not use safety reports to determine whether or not to conduct a legal investigation. (T-1) If initiated, criminal investigations take precedence over safety investigations until criminal activity has been ruled out as possible causes of damage, injury, or death (for criminal investigations, see paragraph 5.11.2).
AFI 51-307, Aerospace and Ground Accident Investigations: 1.2. Purpose of Accident Investigations, 1.2.1. The purpose of an Accident Investigation Board is to conduct a legal investigation to inquire into all the facts and circumstances surrounding Air Force aerospace and ground accidents, to prepare a publicly releasable report, and to obtain and preserve all available evidence for use in litigation, claims, disciplinary action, and adverse administrative action.

## Slide 9: Where Will SIB Support Come From?
The Commander of the Regular AF installation nearest a mishap will provide logistical and investigative support as required.
This applies to the following:
  Clerical help and other personnel as required (WG/SE)
  Office space with secure storage capability (WG/SE)
  Hangar space for the wreckage (EOC/CC, MXG)
  Communications, food and water, transportation, shelter, specialized clothing (WG/SE)
  A contracting officer to assist the SIB with any additional locally procured items (WG SE, FM)
  etc, etc, etc…..
Wing Safety Office is SIB’s starting point
Notes: The nearest active duty base will provide the support the SIB needs and is considered the host installation for the SIB unless authorized by the convening authority…
DAFI 91-204: 2.6. The Commander of the Regular AF installation nearest a mishap. This includes AF-led Joint Bases or alternate organization as designated by the Convening Authority. The commander will ensure the following are accomplished by the appropriate agency: [Reference 2.6. subparagraphs for detailed roles and responsibilities for the Commander of the Regular AF installation nearest a mishap.]
2.6.2. Provide logistical and investigative support as required.
For some OCONUS locations the nearest USAF base may not have airflow capability to meet the ISB or SIB needs. For example: for mishaps occurring in Africa, Aviano may well be the closest USAF base, but they lack heavy A/C capability to put team members in place. Work with USAFE, PACAF and AFCENT as needed to determine what agreements are in place or are needed to support the SIB.
Per DAFI 91-204 2.6.2.1 “The Regular AF wing/delta and GSU or ARC unit should coordinate support through MOA/MOUs.” So, it may take some coordinating with the CA to determine who’s paying for what.

## Slide 10: Investigation Timeline
Mishap, ISB Actions, Prelim Message
SIB Arrival
Finish SIB (Exhibits & Final Message in AFSAS)
Transfer Evidence (AIB, Host Installation JA, etc.)
Brief Convening Authority
Day 1
+3
+30
+40-45
Notes: Typical SIB timeline. However, 30 Days is a should, not a will
Some SIBs won’t fit in a 30 day window despite your best efforts, if need extension request from the convening authority and release 30-day status message
Left: A-10 mishap, Aug 96, aircraft crashed in a swamp in eastern Maryland during an FCF sortie, pilot fatality. Swamp was 2 miles from nearest road (figuring logistics of getting recovery equipment to the site extended the timeline) plus 2 hurricanes occurred right after the mishap that delayed wreckage recovery effort. Picture shows IO standing at crater on day 30.
Right: Dover C-5 mishap, Apr 06. Aircrew in hospitals in Philly 1½ hours away, complicated interview process, extended timeline past 30 days.
Our job finishes after the Convening Authority (MAJCOM Class A, NAF Class B) out briefing, CA Quality Control Review, AFSEC Quality Control Review, and safety report is released in AFSAS.
DAFI 91-204: 9.3. Reporting Schedule. The reporting schedule for each mishap class is shown in Table 9.1.
9.3.1. Number of days shown are measured from the mishap date.
9.3.4. If an investigation is not complete a status message is required at day 30. (T-1) A status message is required at least every 30 days thereafter until the investigation is complete. (T-1)
9.3.5. Class A and B mishap final message timeline includes 30 days for the investigation, 15 days to brief the Convening Authority, and 3 days to release the message after the brief. Exception: For mishaps where an engine or engine module is processed through depot the timeline is 90 days. (T-1)
DAFI 91-204: 8.14. Transferring and Disposing of Evidence. Once the SIB has completed their investigation all non-privileged evidence is either provided to the Accident Investigation Board or other legal board, the host installation Staff Judge Advocate, or returned to the owning organization. [Reference 8.14. sub-paragraphs for detailed evidence transfer guidance]
DAFI 91-204: 10.1. General Information. Safety investigations are considered complete when the safety report is released in AFSAS.

## Slide 11: Investigation Timeline
Investigation can be broken into three 10-day periods:
  Days 1-10 -- Gather the evidence, “What happened?”
  Days 11-20 -- Analyze the evidence, “Why did it happen?”
  Days 21-30 -- Write the report, prepare the briefing, final message
Notes: We can break the investigation into 3 phases……………….
Obviously some overlap will occur between all 3 phases, however this is the general, subjective flow through the 30 days.

## Slide 12: Investigation Flow
Mishap
Investigation
Factors
Findings
Causes
Recommendations
Determine and reconstruct the sequence of events
Any act or issue that affected the outcome of the mishap, whether causal or not
Mishap overview in chronological order containing factors and events that sustain the mishap sequence
Findings that explain why the mishap occurred
Report
Write the report
Feasible Actions which are intended to prevent recurrence of a similar mishap
Notes: Without regard to a timeline, here is how the investigation progresses
We have established the “what” and “why” of the mishap sequence
We are currently building the “what” (Day 1-10)

## Slide 13: SIB Deliverables
Brief to CA Final Message
Safety Report
Notes: 3 products the SIB will produce
Safety Report - Exhibits and data, which are entered into Air Force Safety Automated System (AFSAS), the AF’s computerized program of record for mishaps, recommendations, and mitigating actions.
  The briefing produced by the BP given to the convening authority at the conclusion of the investigation which is also entered into AFSAS as an exhibit within the “Safety Report”
  The final message (mishap narrative, findings, causes, recommendations, etc) which is also entered into AFSAS as part of the “Safety Report”
Although work on each of these will be occurring throughout the SIB process, days 21-30 is when we’ll be finalizing these products prior to deconvening and proceeding to the CA Out-brief.
DAFI 91-204: 8.11. Safety Reports. Detailed information about events are organized and assembled into safety reports. Safety reports consist of the approved final or final supplemental message, and all exhibits.

## Slide 14: Getting Started - Overview
BP Courtesy Visit to the Wing CC
Computer support / SIB Drives
  One network computer per SIB member
  High-capacity duplexing scanner
  Photo capable copier
  Limited access shared drive on server or SIB LAN
  24/7 computer support
  Back-up your working files daily – Recorder
All Primary SIB members need an AFSAS account
  BPs discretion for Secondary members
  Host WG/SE rep to create; MAJCOM/SE to accelerate approval
  Make sure all have elevated access and the proper roles
  See DAFMAN 91-223 para 2.3.4. for required AFSAS roles
  All will use for entering their data in AFSAS
DOWNLOAD CURRENT SIB Support (Go) Package in AFSAS
Notes: For the first SIB only meeting…………………..Reference “SIB SUPPORT REQUIREMENTS LIST” and “DAILY SIB TRACKER” (SIB Go Package – Day One Setup folder)
We will need a minimum of 2 to 3 rooms for the SIB, if what the wing gave us is inadequate, we need to let them know ASAP
Classroom sized room for the SIB to accomplish day to day activities, meetings, phone calls, work on analysis and reports, etc
One to conduct interviews in and for transcribing interviews
One for the BP to work on briefing, hold discussions with the convening authority, etc
IT support for the SIB……………….
Wings often times don’t have 6 or 7 spare computers lying around so you might not get their best
SIB Go Package:
AFSAS > PUBS & REFS (Homepage) > GO PKG: SIB/SIO Go Package > View This Publication > SIB_Go_Package_[CURRENT DATE}_zip (Click on the magnifying glass symbol to download the zip)
Have a wing POC for 24/7 computer support, you’ll be working long hours and weekends and that’s when things will break
Allocate the SIB a temporary “Shared Drive” on one of the base servers. Configure the shared drive such that only SIB members have access. The capacity of the shared drive must be at least 100 GB or….
Create a mini-LAN with the SIB computers. Network all computers to each other such that any hard drive can be accessed by any of the other computers.
Be sure the recorder backs up your files DAILY!

## Slide 15: Getting Started – File Plan
File Inventory – Recorder
  Start organizing Filing System ASAP
Electronic Filing System – SIB (Go) Package
  Use existing electronic folders
  Don’t make new/expand unless needed
Overwhelming Volumes of Paper/Evidence the ISB Collected
  SIB will collect more
Filing Cabinets/File Plan
  Exhibits (Req’d/Optional – AFSAS “Worksheet” short link)
    MX/Aircraft/AGE Records
    Medical/Training/Mission Records
    Etc.
Notes: For the first SIB only meeting…………………..Reference “SIB SUPPORT REQUIREMENTS LIST” and “DAILY SIB TRACKER” (SIB Go Package – Day One Setup folder)
Put the recorder to work starting a filing system ASAP. (slide with changeover between SIB showed just a portion of the data gathered to date, need a way to organize)
Download and Review with Recorder the Event “Worksheet” to verify what exhibit and data field items are required based investigation type
- Short Link found in AFSAS at the bottom of the Event Header section when logged in to the Investigation (AFSAS ID #)

## Slide 16: Getting Started – File Plan
Electronic File Plan
One Folder For Each SIB Member
One Folder For Each Exhibit Type
Notes: The SIB (GO) package has a filing system in it. Just move the files to your server and brief the board members on expected use of it.

## Slide 17: Getting Organized to Investigate
Develop an office “game plan”
  Files, meeting schedule, what we know/need to know, etc
Develop a mishap site “game plan”
Review known circumstances of mishap with SIB
  Listen as a group to ISB interviews
  Review written interviews from ISB
  Set up a “reinterview” or “need to interview” listing/schedule
  Review “products” received from ISB
What technical assistance do we have / do we need?
Get copies of:
  DAFI 91-204
  Discipline specific DAFMAN 91-223
Enter Mishap Report into AFSAS (if not created by ISB or WG/SE)
Notes: Remember we need to get organized to investigate, we aren’t going to solve the mishap on day 1
Listen to the interviews the ISB conducted as a group
  From the interviews get a feel for the “what” of the mishap and the mishap sequence
  Take notes for follow up interviews
  Based on what we’re hearing, what tech support does it look like we need be asking for
  Determine if others need to be interviewed
Develop a crash site game plan
  Who needs to go out to the crash site (usually always MX member, possibly pilot member, not IO (depends on circumstance of the mishap), needs to be organizing the investigation)
  What are we looking for in the wreckage
  Begin to think about when we’re going to recover the wreckage and where are we going to put it
  All SIB members names on Entry Control Letter/Roster
Develop an office game plan
  Recorder developing and setting up file plan
  Post SIB phone #’s and address
  Do we have all the support we need (computers, high speed scanner, a copy of Adobe Acrobat for PDFing report exhibits, shredder, printers, etc)

## Slide 18: Getting Started Protecting Privileged Safety Info
Electronic files
  Don’t transfer outside SIB firewall unless:
    Approved
    Password protected
    Each page bears privileged warning statement!
Paper products must bear privileged warning statement
Notes: A couple “got yas” for the SIB right off the bat that are important from day 1
Protection of privileged information…………………………
DAFI 91-204: Chapter 4, PRIVILEGED SAFETY INFORMATION
[Review Chaper 4 for detailed guidance on handling, marking, and transmitting Privileged Safety Information (PSI)]

## Slide 19: Privileged Safety Information
Privileged Safety Information (PSI) is exempt by law from disclosure out of AF Safety Channels. Includes…
  Testimony given to Investigators under a Promise of Confidentiality (e.g. Witness Statements)
  Information obtained from contractors based on privileged information or under a Promise of Confidentiality
  Investigation deliberative process (e.g. SIB Analysis, Findings, Recommendations, etc.)
  Reports and briefings produced by Safety Investigation Boards
Non-privileged information is “factual” information about a mishap
  Date, time, place, type vehicle, tail number, unedited pictures of the crash site, etc
  Information obtained from contractors (not based on privileged information or under a Promise of Confidentiality)
Notes: But what is “privileged safety information.”
To over simplify, facts are considered non-privileged, analysis is considered privileged.
We’ll be working with both types of information.
Some examples of non-privileged information:
Aircraft tail number
Mishap date
Factual pictures of the crash site
Aircraft Maintenance Records
Raw FDR data as downloaded directly off the FDR
Etc, etc., etc.
Some examples of privileged information:
SIB analysis (Factor or NFWOD analysis, findings, causes, recommendations, etc)
SIB analysis of what's contained in the Aircraft Maintenance Records
Interviews were witnesses are offered the promise of confidentially
Etc, etc., etc.
Again, review DAFI 91-204 Chapter 4 for detailed information on handling, marking, transmitting Privileged Safety Information.
DAFI 91-204: 8.4. Obtaining and Using Technical Assistance and Laboratory Analysis.
8.4.1.2. SIBs must ensure a “Non-Disclosure Agreement-Safety Investigation-DoD Personnel” or “Non-Disclosure Agreement-Safety Investigation-Contractor Rep” (as applicable) on protection of privileged data is prepared and endorsed by all non-DAF SIB personnel (e.g., contractors, National Transportation Safety Board) offered a promise of confidentiality or provided access to privileged safety information. (T-1) The SIB must use the templates located in the SIB Go Package. (T-1)
8.4.2. Technical experts will author either a non-privileged or privileged report; in some circumstances, they may author two reports, one non-privileged and one privileged. (T-1) If a contractor representative is granted a promise of confidentiality for their technical report the DAF maintains sole possession or control of the report, and all the contractor representatives’ notes, drawings, etc., must be turned over to the SIB or destroyed. (T-1)
8.4.2.2. Privileged technical reports contain the technical expert’s analysis, conclusions, and recommendations based on privileged information to include confidential statements or SIB member deliberations.
8.4.2.2.1. Privileged technical reports are not meant to duplicate information provided in non-privileged technical reports. They provide supplemental analysis and conclusions to assist the SIB in determining causes and recommendations. A privileged report is not required if technical expert analysis and conclusions can be based solely on physical evidence, factual information, and statements made without a promise of confidentiality.

## Slide 20: Privileged Safety Information
Protects the process by limiting access to SIB analysis
  No restaurant or bar talk!
  No talking to colleagues, friends, or family!
NDAs for tech assist reps (contractors) and other “outsiders”
Notes: To protect the safety system and to ensure that people are forthright with SIBs privilege exists to prevent the analytical and speculative portions of the investigation from being used for any non-safety related purposes, i.e. litigation.
To protect privilege, SIB members are not allowed to talk about the mishap outside of the investigation. If we need to talk to someone (think interviews) we determine whether or not they require the Promise of Confidentiality (because we feel they are holding back information) and offer them a Promise of Confidentiality (or not), or we use people that are a part of the process, namely the Convening Authority Safety staff and/or AFSEC support.
If you are in doubt or have questions, ask me and if I don’t know the answer, I’ll find it.
Review AFSEC/JA PSI Refresher Video at this link: (AFSEC Portal Page > JA > Protecting Privileged Safety Information Video)
AFSEC - Air Force Safety Center (AFSEC) - Privilege Training
DAFI 91-204: 4.4.3.2. All persons (except the Convening Authority, his/her staff, safety office staff, and AFSEC personnel) given or provided access to privileged safety information by the ISB or the SIB prior to the Convening Authority briefing must agree to and sign the appropriate safety privilege agreements. (T-1) These agreements include: “Non-Disclosure Agreement-Safety Investigation-DoD Personnel”, “Non-Disclosure Agreement-Safety Investigation-Contractor Rep”, or “Privileged (Confidential) Witness Agreement”. Use the templates located in the SIB Go Package or the ISB Go Package. Personnel who are not exposed to safety privilege (e.g., personnel guarding or assisting in recovery of mishap wreckage) do not sign non-disclosure agreements.
DAFI 91-204: 8.4. Obtaining and Using Technical Assistance and Laboratory Analysis. 8.4.2.2.2. SIBs must ensure authors sign a “Non-Disclosure Agreement-Safety Investigation-DoD Personnel” or “Non-Disclosure Agreement-Safety Investigation-Contractor Rep” (as applicable). (T-1) SIBs must upload the signed non-disclosure agreement as an exhibit in AFSAS. (T-1) The DAF maintains sole possession or control of the report. All the contractor representatives’ notes, drawings, etc., must be turned over to the SIB or destroyed.

## Slide 21
Witness Interviews

## Slide 22: Interviews
Review DAFI 91-204 8.3, Written and Verbal Testimony AND the Safety Investigator SIB Interview Guide found in the SIB Go-Package prior to conducting any interviews.
Ensure SIB has copies of all the required interview forms from the CURRENT SIB Go Package prior to conducting any interviews.

## Slide 23: Interviews
Brief interview status everyday at the daily SIB meetings
  Reference “Interviewees” Tab in Daily SIB Tracker
What interviews are we doing today?
  Who is doing it?
  What questions are we asking?
  What are we trying to find out?
Which interviews are left to accomplish?
Which interviews are we going to transcribe?
What is the status of the interviews we are transcribing?

## Slide 24: Privilege
Who can authorize the offering of the Promise of Confidentiality?
  Designated SIB members (BP & IO)
  Single Investigating Officers
When is a promise of confidentiality authorized?
  Only for aircraft, missile, space, nuclear, friendly fire, DEW mishaps (or AF/SE permission)
  Only when needed to encourage frank and open cooperation
  Factors to consider:
    Requests, gaps, hesitations, reluctance, etc.
    Involvement in mishap sequence
    Not all witnesses need/require promise of confidentiality
Who can be promised confidentiality?
  Any witness, Analysts, OEM
  Anyone who may be reluctant to talk
Notes: At the SIB level it’s the BP and IO that’s authorized to offer a promise of confidentiality.
Ensure each interview, whether it is provided under a promise of confidentiality or not, is properly documented (use the CURRENT Privileged and Non-Privileged Witness Agreements found in the SIB Go-Package).
Remember, at the beginning of each interview to read and record the appropriate privileged or non-privileged opening script in accordance with DAFI 91-204, who is being interviewed, the date, who is doing the interview, etc. Again, at the end of the interview read and record the closing script.
If a witness has provided more than one written statement and/or verbal testimony, each instance requires a separate signed Witness Agreement identifying the nature of the testimony (i.e. whether it was given under a promise of confidentiality or not). (Example: Mishap Pilot gave a written statement to the ISB and gave a verbal testimony to the SIB, both under a Promise of Confidentiality. There should be two separate Privileged (Confidential) Witness Agreements fully filled out and signed by the Mishap Pilot indicated that they were offered and understand the offer extended to them.)
DAFI 91-204: 4.5.3. Persons Authorized to Offer Promises of Confidentiality. Only the ISB President, ISB Investigating Officer, SIB President, SIB Investigating Officer, or an SIO may offer promises of confidentiality and only during safety investigations where promises of confidentiality are authorized. When conducting safety investigations in which promises of confidentiality are authorized, the SIB President/SIO and SIB Investigating Officer have the sole discretion to decide who will be offered a promise of confidentiality. The authorized official’s decision shall not be made on a blanket basis, but must be based upon a witness or contractor’s reluctance to cooperate or apparent self-interest in not disclosing information. After deciding to offer a witness confidentiality, the SIB and ISB President may authorize other board members to extend that approved offer to the witness or contractor.

## Slide 25: Interview Forms
Download from the CURRENT ISB/SIB Go packages
    AF Portal or AFSAS Pubs and References page
Use the appropriate forms outlined in the ISB/SIB Interview Guides
  Follow the Documentation Instructions on which sections to complete for Written Statements or Recorded Interviews

## Slide 26: Interview Forms
AF Portal/AFSEC/SIB Support
Notes: Where can the SIB find these forms?
SIB support documents found on the Air Force Safety Center Portal site or in AFSAS under “SIB Go Package”
Link: SIB Support (SIBSupport) (af.mil)

## Slide 27: Gathering Data Interviews
SIB interviews help determine what happened
  Only determine who needs to be interviewed after reviewing all ISB interviews
  Interview other witnesses not interviewed by ISB ASAP
Interviews establish a direction for the investigation … or not
Witness statements and physical evidence go hand-in-hand in determining the cause; they complement or clarify each other … or not
Witnesses include: Surviving crew, MX, ATC, eye witnesses, tech experts, etc.
Record all interviews
Notes: Initial interviews were accomplished by the ISB………………………..
In this phase we’ll be accomplishing follow-up interviews, interviews with folks the ISB might have failed to interview and initial interviews with personnel we determine we need to interview as the investigation progresses.
In the ISB interviews they only asked one question………………….. “Tell me what happened”
We’ll be expanding on that during the SIB with specific questions aimed at narrowing down why the mishap occurred……………………..

## Slide 28: SIB Interviews, Privileged & Non-Privileged
Rules:
BP, IO authorized to offer promise of confidentiality
Document interviews using appropriate forms from the CURRENT SIB Go Package
Read the provided scripts into the recorder
Use two recorders (incase one fails)
Each interview and/or written statement requires its own witness agreement
Notes: At the SIB level it’s the BP and IO.
Ensure each interview, whether it is provided under a promise of confidentiality or not, is properly documented (use the CURRENT Privileged and Non-Privileged Witness Agreements found in the SIB Go-Package).
Remember, at the beginning of each interview to read and record the appropriate privileged or non-privileged opening script in accordance with DAFI 91-204, who is being interviewed, the date, who is doing the interview, etc. Again, at the end of the interview read and record the closing script.
If a witness has provided more than one written statement and/or verbal testimony, each instance requires a separate signed Witness Agreement identifying the nature of the testimony (i.e. whether it was given under a promise of confidentiality or not). (Example: Mishap Pilot gave a written statement to the ISB and gave a verbal testimony to the SIB, both under a Promise of Confidentiality. There should be two separate Privileged (Confidential) Witness Agreements fully filled out and signed by the Mishap Pilot indicated that they were offered and understand the offer extended to them.)
Keep in mind the difference between testimony and evidence. Example: Under a promise of confidentiality a mishap pilot testifies that he left the gear handle up during the mishap sequence. If another crewmember provides the same testimony during a non-privileged interview or if physical evidence confirms the gear handle was up during the mishap sequence, that evidence is NOT privileged. The TESTIMONY the mishap pilot provided under a promise of confidentiality is privileged, however evidence uncovered outside that interview may not be.

## Slide 29: Witness Interviewing
Who should do the interviewing?
  Area expert - maybe
  Who is available
  People person
  If two are sent -- only one does the interview
  Don’t allow “observers.” They can listen to the recording afterwards.
Notes: Who would you pick?
The area expert.
Keep the interviewing crowd to a minimum to keep from intimidating the witness
One on one is best
If two accomplish the interview, not a good cop/bad cop scenario
BP does interviews at the senior staff level
Witness can be compelled to meet with interviewer by CC/Shirt, but not what to say.
Consider ending questions…
Is there anything I didn’t ask that you would like to add?
DAFI 91-204: 8.3.5.6. If a witness refuses to be interviewed or provide a statement, contact their commander, Convening Authority safety office, or AFSEC/JA, to discuss lawful orders to participate.

## Slide 30: Witness Interviewing
  Not an interrogation
Do not have witnesses testify under oath or give sworn testimony
NO truth serums, hypnotic techniques, drugs, or polygraph tests
If a witness provides a statement under medication, add a notation to their statement
Ensure witnesses understand that they are obliged to give honest, good faith testimony
  If criminal misconduct is suspected, contact HQ AFSEC/JA on how to proceed
Notes: Basic Interview ROE………………………..
DAFI 91-204: 5.11. Special Circumstances.
5.11.2. Events Involving Potential Criminal Acts. If safety investigators discover evidence of criminal acts causal to the event, they must immediately stop investigating and notify AFSEC/JA and the Convening Authority. (T-0) If there is credible evidence of criminal activity the Convening Authority shall notify the responsible military or civilian law enforcement organization. (T-0) The Convening Authority will determine if and when the safety investigation should continue, and the scope of that investigation. (T-0) Office of Special Investigations inquiries take precedence over safety investigations of fatal events until criminal activity has been ruled out as a possible cause. The Convening Authority will give all non-privileged material to the legal investigators, provide them with the names of all witnesses, and safeguard all privileged material. (T-0) A use of force review board initiated in accordance with AFI 31-117, Arming and Use of Force by Air Force Personnel, does not take precedence over a mishap investigation.

## Slide 31: Witness Interviewing
Script interview questions and leave space for answers
Interviews typically go from general questioning to specifics
  From “Tell me what happened … ” to “Which checklist did you apply and why … ”
  May take 3 to 6 interviews with mishap participants
  Take notes to highlight details for further questioning or investigation
Notes: We’ll typically do multiple interviews with mishap principles (pilot, maintainers if mx was a factor, etc)
Questions will get more focused as interviews progress
BE SURE THAT IF FOLKS COULD USE SOMETHING IN THE EXECUTION OF THEIR JOBS YOU HAVE IT AVAILABLE FOR THEM TO REFERENCE SO THEY CAN TELL YOU EXACTLY WHAT THEY DID. (CHECKLIST, T.O., ETC)
DON’T MAKE THEM GUESS AT THE STEPS THEY DID OR DIDN’T ACCOMPLISH……..

## Slide 32: Witness Interviewing
Establish a polite & professional rapport
  It is not an interrogation
Let them talk –
  Do not interrupt a witness while they are narrating an event
Question in a logical sequence -- Don’t lead the witness
Don’t argue / disagree / disapprove
Don’t let witness question you
Don’t share information from other interviewees
  “In his interview Capt Matthews mentioned … ”
  Violates Privilege
Not necessary to publish every statement taken from every individual in the Testimony and Statements exhibit group. Don’t transcribe interviews that won’t go into the report
Notes: ALL ARE IMPORTANT………………………..
READ EACH BULLET

## Slide 33: Interviews - Problem Areas
Not completely filling out required forms – need all information
Not reading/recording the provided opening and closing script
Not starting transcriptions early enough
Finding Transcribers
  AFSAS Transcription (Reference SIB Go Package Guide)
  Transcribing/Reviewing testimony will be most time-consuming, labor intensive duty of SIB support
Notes: With respect to transcribing…………………………
Emphasize
Get started early on transcribing interviews you plan on using in the report. Don’t put it off or stiff arm it……….transcribing/reviewing testimony will be extremely time-consuming, labor intensive duty for clerical support and SIB members.
Person Transcription: For every 1 hour of interviews it takes approx 7 hours to transcribe correctly and QC.
AFSAS Transcription: For every 1 hour of interviews it takes approx 3 hours to transcribe correctly and QC.
After its transcribed have somebody on the SIB sit down and listen to the tape and read the transcription as the tape plays to ensure it is correct.
Review required - Transcribers don’t speak aviation and often get our vernacular wrong………………..
  Papi = Happy (I had the happy lights in sight)
  SA = Essay (I could tell I was losing my essay)
  On the C-5 SIB one of the pilots transcriptions said “I have an itchy back” In reality he said “Lets get back to the checklist.” Huge difference intent and meaning.
Take the time to get transcriptions right ……..and it will take longer than you think.

## Slide 34: Gathering Data Surveys
Notes: Coordinate with HQ AFSEC Aviation Psychologist for assistance with conducting appropriate surveys.
Another way to gather data is through surveys.
Surveys can be used within the mishap unit or sent to other units to help the SIB resolve questions or gray areas………………….
For example, in this survey, used following an F-15 mid-air collision (19 Aug 99 Lambert) the SIB, based on pilot testimony and review of blind procedures and guidance, determined that guidance ambiguity on “exactly when to call blind” may have been factor in the mishap.
Note: will need to define “blind” for non-aviators in the group
This survey was developed and sent out the F-15 community via wing FSOs to determine their perception of when to call blind during BFM (172 responses: 88% said they would not wait longer than 5 seconds, 5% thought 5-10 seconds was reasonable, 2% thought a blind call is not required if maintaining a predicable flight path, etc. SIB determined this was not a factor because calling blind is basic and endemic in a fighter pilots training and habit patterns)

## Slide 35: Release of Information ...
Who can a SIB release information to?
  The CA – Yes
    The SIB works solely for the CA
  CA/SE Staff – Yes
  Rest of the CA staff – No
  AFSEC – Yes
  What about mishap Wing/CCs …NO!
    ISBs/SIBs make no decisions on aircraft or personnel flight worthiness but…..
Notes: WE WORK FOR THE CA DIRECTLY SO WE CAN RELEASE INFO TO THEM…….
2 STAR MX CC? – NO, THAT REQUEST IS COORDINATED THROUGH THE CA
MAJCOM SAFETY STAFF – YES…..WE ARE WORKING WITH THEM TO COMPLETE THE INVESTIGATION AND THEY UNDERSTAND NOT TO RELEASE INFORMATION
AFSEC - YES…..WE ARE WORKING WITH THEM TO COMPLETE THE INVESTIGATION, TECH SUPPORT ISSUES, ETC.
WING CC OR WING SAFETY STAFF – NO, unless they are the convening authority, WHY NOT?
ALL OTHERS ARE SPECIFICALLY EXCLUDED FROM THE FLOW OF INFORMATION IN ORDER TO PREVENT OPPORTUNITIES FOR OTHER COMMANDERS TO UNDULY INFLUENCE THE SIB INVESTIGATION AND FINDINGS
THE APPROPRIATE AVENUE FOR WING COMMANDERS TO REQUEST INFORMATION FROM AN SIB IS THROUGH THE CONVENING AUTHORITY.
DAFI 91-204: 2.10. The SIB will: Work solely for the Convening Authority while accomplishing the requirements outlined in this instruction. (T-2)

## Slide 36: What if … Release of Information
Investigators discover information which seriously impacts the operation of a weapon system.
  Immediately notify the Convening Authority, regardless of whether such information is associated with the mishap currently under investigation.
  Convening Authority will notify other action agencies, the appropriate program manager for the weapon system or items involved, the weapons system lead command, and the AF Safety Center. These action agencies must evaluate the nature and seriousness of the information, determine the proper response, and issue required instructions.
Notes: This is the process…………………..
Contact the convening authority safety office and relay the information. Let them determine the next step………………..then get back to investigating
DAFI 91-204: 2.9. The SIB President or SIO will:
2.9.5. Upon discovery of information that seriously impacts the safe operation of a weapons system or endangers personnel, immediately notify the Convening Authority, and potentially the unit commander if the Convening Authority notification cannot be made in a timely manner, regardless of whether such information is associated with the mishap currently under investigation. (T-1)
2.5. The Convening Authority chosen in accordance with Paragraph 5.2 will:
2.5.7. Upon receiving notification of a critical safety concern take the following actions:
2.5.7.1. Notify other action agencies, the appropriate program manager (for joint programs the program manager is considered to be the Joint Program Office or equivalent) for the weapon system or items involved, the weapons system lead command (AFPD 10-9, Lead Command Designation and Responsibilities For Weapon Systems), and AFSEC. (T-1) These action agencies must evaluate the nature and seriousness of the information, determine the proper response, and issue required instructions. (T-1)
2.5.7.2. Ensure the program manager has access to specific technical information and other critical information as it becomes available so the program manager can meet airworthiness responsibilities required by AFI 62-601, USAF Airworthiness, and Life Cycle Systems Engineering responsibilities required by AFI 63-101/20-101, Integrated Life Cycle Management. (T-1)
2.5.7.3. Ensure originating units send critical safety hazard information to appropriate agencies in accordance with AFI 11-215, Flight Manuals Program, and Technical Order 00-5-1, AF Technical Order System. (T-1)
2.5.7.4. As quickly as practical, forward all critical safety information related to military variants of civil aircraft and commercial off-the-shelf aircraft and equipment to the AFSEC Flight Safety Division (AFSEC/SEF). (T-1) AFSEC/SEF will ensure all such information contributing to the promotion of aviation safety is forwarded to the Administrator of the Federal Aviation Administration (FAA) and/or the Chairperson of the National Transportation Safety Board for appropriate action without disclosing privileged safety information.

## Slide 37: Technical Support
Tech assist ROE:
  Requested by SIB through AFSEC
Technical Assistance Duty Officer (TADO)
  DSN 246-5867
  Commercial 505-846-5867
  After Hours 505-220-0183
  Do not directly contact contractors or vendors for teardown and analysis without speaking to HQ AFSEC/SEFE (TADO) first.
  Normally reps paid by SPO under contract
  Outside labs/specialists may need contractual vehicle
Notes: For technical assistance the SIB requires………….
Do not directly contact contractors or vendors for teardown and analysis without speaking to the System Manager or HQ AFSEC/SEFE first.

## Slide 38: Technical Support
Two general types of “technical support”
  The manufacturer/contractor that designed, built or maintained the equipment (such as GE, Lockheed Martin)
  DOD military/civilian personnel (such as ALCs, SPO, Depot, AF Labs)
The distinction is important…….
Notes: Self explanatory, read entire slide

## Slide 39: Technical Support
If DoD personnel (civilian or military) provided written reports include them in the Technical and Engineering Reports exhibit with the appropriate attributes.
Do not provide a promise of confidentiality to DoD personnel for a non-privileged report.
However, as with all persons provided access to privileged safety information by the SIB ensure they sign the “Non-Disclosure Agreement - Safety Investigation-DoD Personnel” (SIB Go Package) and it is on file with the SIB.
  Keep on file with the SIB (Recorder – File Plan)
    NDA exhibit.
Notes: Self explanatory, read entire slide

## Slide 40: Technical Support
Contractors/Manufacturers are required to sign the “Non-Disclosure Agreement - Safety Investigation - Contractor Reps” (SIB Go Package) as Technical Experts to Safety Investigations.
If Contractors/Manufacturers ask for a promise of confidentiality, they are required to complete a Privileged Witness Agreement to be placed before the report.
  Proprietary company information…not a driver for PSI
A privileged technical report may contain analysis, conclusions and recommendations based on privileged information to include confidential statements, appointed SIB member deliberations.
Notes: Proprietary information is protected from public release under CUI registry guidance, and should not be the basis for a Contractor/Manufacturer requesting a promise of confidentiality
- If a contractor requests a promise of confidentiality, recommend calling AFSEC/SEFE TADO for input on the best way forward.
DAFI 91-204: 8.4.2.1.4. A contractor’s proprietary information does not make a report privileged, but requires appropriate markings so affected portions are not publicly released. The DAF maintains sole possession or control of the report, but the contractor representative may retain their notes, drawings, etc.

## Slide 41: Technical Support
Often times however they do not request a promise of confidentiality.
    For example Lockheed Martin just gives you a factual analysis of the continuity of the flight control system following a mishap. It will also go in the Technical and Engineering Reports exhibit with the appropriate non-privileged attributes.
Notes: Self explanatory, read entire slide

## Slide 42: Tracking Parts Analysis
Evidence Analysis will be taking place either…
  In the SIB “offices”
  At mishap site
  In a local hangar
  At the contractors/experts
Bottom Line…..
Know….
  Where aircraft or equipment parts are
  Who is doing what to them
  What do you expect from the analysis
  When they are due back
  Brief at daily meeting
  Reference: Daily SIB Tracker “Release & Analysis Tracking” Tab
Notes: As parts are shipped off for analysis, we need to keep track of:
Who has them
When they were shipped
What are you hoping to find out from the teardown
When do you expect the results of the analysis
Another topic to brief at the daily meetings………..

## Slide 43: Mishap Analysis & Animation Facility (MAAF)
Central DAF agency for recovery, transcription, analysis, simulation, and animation of all data in support of SIBs (DAFMAN 91-223)
Primary source for animations intended to represent the actual mishap sequence
Contact the MAAF through the technical assistance hotline
MAAF has organic capability to recover data from damaged recorders
MAAF produces plots, tabular listings, copies of CVR and animations
Notes: Another form of Technical Support is the MAAF located at AFSEC………….
For flight mishaps the MAAF is your source for downloading FDRs/CVRs
The MAAF will produce your animations if you need one…..
Contact the MAAF through the technical assistance hotline as shown on previous slide - DSN 246-5867 Commercial 505-846-5867
DAFMAN 91-223: 6.5.3.2. The AFSEC Flight Safety Engineering Branch (AFSEC/SEFE) Mishap Analysis & Animation Facility (MAAF) is the central DAF agency for recovery, transcription, analysis, simulation, and animation of all data in support of SIBs. AFSEC/SEFE will be the primary source for animations intended to represent the actual mishap sequence. (T-1) The SIB’s use of simulation and animation products and tools, including those generated from contractor simulators, test range data systems, training range data systems, tactical data links, and companion aircraft will be reviewed by the MAAF to ensure the validity, limitations, and appropriate use are addressed. (T-1)
6.5.3.2.1. Animations are commonly created to allow SIBs to see multiple data sources merged together. MAAF personnel will be the primary source for animations intended to represent the actual mishap sequence. (T-1) Animations produced from data without SIB input are considered non-privileged. If the SIB provides input or direction to the animation creators, then the animation contains privileged safety information and must be marked accordingly. (T-1)
6.5.3.2.2. AFSEC/SEFE does not provide services such as the development or editing of multimedia products to be used solely as briefing aids.

## Slide 44: Mishap Analysis & Animation Facility (MAAF)
MAAF has the capabilities to combine multiple sources of data
  FDR
  CVR
  RADAR data
  Simulator data
  Terrain data
  Mapping data
  HUD tapes
Notes: MAAF can combine many sources of data to produce the animation that best tells your story for the outbriefing and assists with your analysis.
But the more complex the animation the longer it will take for the MAAF to produce it…………..

## Slide 45: Mishap Analysis & Animation Facility (MAAF)
Typical turn around times for products
  Initial readout & plots/tables 1-2+ days
  Copies of CVR 1+ day
  Initial animations 3-5+ days
  Final animation 7-10+ days
Several factors may cause longer turn-arounds
  Recorder damage
  Animating complex mishap scenarios
  Other workload
Notes: Typical turn around times…………………………
Remember the more complex the animation the longer it will take for the MAAF to produce it affecting turn around time…………..

## Slide 46: SIB Members
SIB members will fall into one of three categories:
  Primary members
  Secondary members
  Support members
Notes: We’ll define each and the role they play on the SIB as we go through the briefing…………….. The next few slides shows some basic duties based on SIB role so everyone has an idea of what each other should be doing.
Reference DAFMAN 91-223: Chapter 5 SIB Requirements, 5.1. SIB Membership.
5.1.1. Primary members determine the SIB’s results, including factors, findings, causes, and recommendations. Only primary members authenticate the safety report. See Table 5.2 for minimum SIB membership requirements.
5.1.2. Secondary members provide expertise or assistance to the SIB. Secondary members may participate in all SIB deliberations to the extent authorized by the SIB President, but do not authenticate the safety report. CAs will ensure secondary members for Class A mishaps are not from the mishap wing/delta or equivalent. (T-1) CAs will ensure secondary members for Class B mishaps are not from the mishap squadron or equivalent. (T-1) Individuals identified in Table 5.1 may be added as secondary members. CAs will ensure secondary members are DoD personnel and meet the qualifications, grade, and training requirements in Table 5.1. (T-1)
5.1.3. Support members are observers or other personnel who assist the SIB. Support members can come from depots, industry, civilian organizations, CA safety staffs, other government organizations, and laboratories. The SIB President determines the extent of support member involvement in the SIB. Support members do not need to be DoD personnel.
5.1.4. It is common for SIBs to use other personnel to assist with wreckage and evidence recovery, transcriptions, administrative, or other tasks. These personnel are not members of the SIB. Use of these personnel is at the discretion of the SIB President.

## Slide 47: Board President (BP)
Responsible for all activities of the SIB
Sets the tone for the investigation/board
  Establishes working hours, daily meetings, etc.
Focal point for all public affairs issues
“Top Cover”
Ensures wing/unit cooperation
Reports directly to the Convening Authority
Builds and presents convening authority briefing
  Briefing is BP’s “report card”

## Slide 48: Investigating Officer (IO)
Expertise in mishap MDS not required
Manages daily SIB activities under direction of BP
  Directs and coordinates all phases of the investigation
  Runs daily meetings
  Coordinates timeline compliance with AFSEC Rep
Writes majority of Narrative

## Slide 49: Pilot Member
Mishap MDS expert
  Dash-1, tactics, techniques, etc.
  Identifying wreckage (particularly cockpit)
  Interpret VTR tapes
  Analyses ops factors to include:
    Qualifications
    Proficiency
    Training
    Communications
    Aircrew actions
    Mission-specific concerns
    Performance data
    aircrew stressors
QC transcribed recorded comms
  HUD, CVR, ATC, etc.
Conduct interviews

## Slide 50: Maintenance Member
Maintenance procedures expert
Analyses Maintenance Factors to include:
  Aircraft history
  Aircraft systems
  Maintenance Personnel Qualifications
  Maintenance Personnel Proficiency
  Maintenance Personnel Training
  Evaluates depot and Quality Assurance Actions
  Design or Engineering Deficiencies
Directs aircraft / wreckage recovery
Conduct interviews - maintenance personnel
Directs military technical support
  QA, crew chiefs, etc.

## Slide 51: Flight Surgeon
Graduate of AMIP
Drafts Medical Analysis Exhibit
Interprets medical records and autopsy reports
Aids in human factors analysis
  USAF aviation psychologists / physiologists available
Participates in interviews
  72-hour and 7-day histories
Aids in life support investigation
Advises the SIB on protected health information

## Slide 52: Aircrew Flight Equipment Member (AFE)
Aircrew flight equipment / egress expert
  Verifies correct use / serviceability of life support equipment
  Interviews as required
  AFSEC life support / egress expertise also available

## Slide 53: Human Factors (Fatality)
  Graduate of AMIP or AMIC
  Must be an Aerospace Physiologist, Psychologist
  Fully qualified officer or civilian equivalent
  Analyzes
    Human Factors
    Human Performance
    Ergonomics
    Physiology and Psychology issues
  Collaborates with the Flight Surgeon on this analysis and assigns DoD Human Factors Analysis and Classification System (HFACS) codes.

## Slide 54: AFSEC Representative
Process expert
  Keeps SIB on timeline
  Coordinates for technical assistance
  Provides mishap investigation continuing education
Safety Report “proprietor”
  AFSAS Exhibit Management (Recorder)
  Guides Narrative Writing Efforts (IO)
Notes: Listed are some of the AFSEC reps functions
Bottom-line the AFSEC rep works with the IO to manage the investigation
This position on a SIB was created by the CSAF Blue Ribbon Panel on Safety in 1995.

## Slide 55: Secondary Members
Additional Crew Members
Technical Experts
AFFSA Rep
AFOTEC Rep
Airfield Operations
Crash Fire & Rescue
Cyberspace
Defense Contracting Management Agency
Jumpmaster or Parachute Malfunction Officer
Special Warfare
Weapons
Weather
Other (AF/SE or CA determined necessary and appropriate)
Notes: Other secondary members that could be added……
Again. Will depend on the circumstances of the mishap
These are not voting members on the SIB.
DAFMAN 91-223: 5.1.2. Secondary members provide expertise or assistance to the SIB. Secondary members may participate in all SIB deliberations to the extent authorized by the SIB President, but do not authenticate the safety report. CAs will ensure secondary members for Class A mishaps are not from the mishap wing/delta or equivalent. (T-1) CAs will ensure secondary members for Class B mishaps are not from the mishap squadron or equivalent. (T-1) Individuals identified in Table 5.1 may be added as secondary members. CAs will ensure secondary members are DoD personnel and meet the qualifications, grade, and training requirements in Table 5.1. (T-1)

## Slide 56: Recorder
Office manager and contracting office liaison
  Admin support / transcription supervisor
  Establishes and maintains filing system (start today!)
Tracks everyone associated with mishap and investigation
Assists with all safety report products as needed
Assists with evidence and wreckage handover
Secondary member
  Non-voting
  Backbone of investigation!!

## Slide 57: “Support” Members
Observers or other personnel who assist the SIB
  Depot
  Industry
  Civilian Organizations
  CA Safety Staff
  Other Governmental Organizations
  Laboratories
Notes: A Support Member is one you feel you need to add to the SIB or the convening authority adds based on the circumstances of the mishap.
For example on the Dover C-5 SIB the SIB asked for a Loadmaster and Flight Engineer be added due to aircrew issues/factors in the mishap
Any additional individual skill that you might need – ask for through the convening authority. They have to approve it, don’t just call one of your buddies and ask him/her to join the SIB……………………
DAFMAN 91-223:
5.1.3. Support members are observers or other personnel who assist the SIB. Support members can come from depots, industry, civilian organizations, CA safety staffs, other government organizations, and laboratories. The SIB President determines the extent of support member involvement in the SIB. Support members do not need to be DoD personnel.

## Slide 58: SIB Members
Who is doing what…..
  BP – “Chairing” daily meetings, working on briefing, Supervisory interviews, QC interviews, MAJCOM & Wing liaison for problems, working with On Scene Commander/Recovery Operations Chief for mishap site issues
  IO – running day-to-day investigation, keeping SIB focused
  Primary SIB members – conducting interviews, QC interviews, reviewing/analyzing “data,” writing report
  Contractor/ALC Reps – teardowns of equipment, preparing reports on results of teardowns
  AFSEC Rep – helping IO run/manage investigation
  Recorder – Keeping the admin side running smoothly, ensure interviews are being transcribed, etc.
Notes: By function, who is doing what……….

## Slide 59: SIB Members
DAFI 91-204, 2.10. The SIB will: Work solely for the Convening Authority while accomplishing the requirements outlined in this instruction.
Notes: Previously mentioned.
Why is this important?
Convening authority = MAJCOM commander, not the MAJCOM mx director, MAJCOM ops director, your wing commander
DIRECTLY FOR THE CONVENING AUTHORITY

## Slide 60: Foot Stompers…………
Remember you work for the CA and this is your full-time job.
Save all original documentation for the AIB if one is appointed.
  Pilots training folders/FEF, aircraft maintenance records, etc.
  Make copies for wing if required
The IC is responsible for the logistics (comm, water, port-a-potty, etc) at the mishap site, not the BP!
All persons provided access to privileged safety information by the SIB sign the “Non-Disclosure Agreement - Safety Investigation – DoD Personnel”or “Non-Disclosure Agreement - Safety Investigation – Contractor Rep” and it is kept on file with the SIB.
Notes: Foot stompers, read each one and emphasize.

## Slide 61: SIB is the Priority
Let BP know immediately of potential distractions
  Marital problems
  Health problems
  Family problems
  Financial problems
  Education
  PCS
  Separating
Notes: Over the next 30 days, we have one priority – the completion of this investigation.
If anyone has any distractions of any sort, that may prevent them from giving 100 percent of their time and effort to this SIB, please let the Board President know immediately.

## Slide 62: In Closing.…
To help you navigate the process there is a Class A and Class B SIB Techniques Guide in AFSAS “Pubs & Refs”
Notes: To help you navigate the process there is a Class A and Class B SIB Techniques Guide in AFSAS under “Pubs & Refs”

## Slide 63
Factor Analysis
(Brief on or about Day 7)

## Slide 64
Analysis

## Slide 65: Investigation Flow
Mishap
Investigation
Factors
Findings
Causes
Recommendations
Determine and reconstruct the sequence of events
Any act or issue that affected the outcome of the mishap, whether causal or not
Mishap overview in chronological order containing factors and events that sustain the mishap sequence
Findings that explain why the mishap occurred
Report
Write the report
Feasible Actions which are intended to prevent recurrence of a similar mishap
Notes: We have established the “what” of the mishap sequence
We are now preparing to move from the “what” to the “why” (Day 11-20)

## Slide 66: What to Why
Without finding “The Why,” the failure will occur over and over
Keep asking “Why” until reaching a dead end
  Elevator fell off … Why?
  Bolt failed ... Why?
  Improperly installed ... Why?
  T.O. wrong ... Why?
  Not field tested ... Why?
  No requirement to field test … Bingo!
Notes: The key here is to keep asking why…..
Start with the last event in the mishap sequence and work backwards, keep asking why………..
The unanswered “whys” is where the investigation needs to be focusing.
For example…………..
Note: The line represents where most inexperienced investigators stop.
There Is A Temptation to Grasp at First Plausible “Why,” Cease Investigating and Start Writing
Recommendations to fix the bolts will not keep this mishap from happening again.
We need to get to the root cause, the bolt failure is not the root cause.

## Slide 67: What to Why
The investigation needs to be done in a sequential and consistent manner so all relevant facts are collected before any conclusions are drawn
DO NOT CONCENTRATE ON ANY ONE AREA EARLY TO THE EXCLUSION OF OTHER AREAS
ENSURE THE FACTS LEAD TO THE CONCLUSION, RATHER THAN THE OTHER WAY AROUND!
Notes: Several other keys during this period…………………
Emphasize… ENSURE THE FACTS LEAD TO THE CONCLUSION, RATHER THAN THE OTHER WAY AROUND!
Don’t take your day 1, walking in the door, based on what I know about the mishap theory and try to make the facts fit it (inexperienced investigators do this too)
Keep asking why………………..

## Slide 68: What to Why
Plot out mishap sequence
  Will help in identifying both factors and non-factors
  Serves as a starting point for identifying findings
Now for the white boards …
Notes: Ways to help organize your thoughts……………..
Offer 2 techniques for plotting out the mishap sequence and to help identify root cause or causes
Now for the white boards…………..

## Slide 69: Fault Tree Analysis
Starts with the significant event
List possible causes at next level
Each cause now becomes a significant event with analysis listed below
For each potential cause, list probability
When probability nears zero, you are done in that direction
Visually shows logic
Brainstorm all possible causes
Notes: One way as a group to brainstorm all the possible reasons the mishap might have occurred is to use a Fault Tree Analysis (one of the reasons we’re going to need a lot of white board space)
Starts with the mishap and brain storms all possible causes to rule them in or rule them out……………….

## Slide 70: Fault Tree Analysis
Pilot does not eject - Fatality
Pilot
Incapacitation
Analysis:
-On controls impact
-CVR
Ejection Seat
Failure
-Handles down
-Actuators unfired
Analysis
Thought
Recoverable
Continue
- Review recorders
- Determine HFs
Stop
Stop
Focused on
Improper Recover
Procedure
Continue
- Review standard
- Review recorders
- Eval/Trng History
- Survey?
Notes: Example………….aircraft fails to recover from a spin, pilot does not eject.
Very simplistic example
Group brainstorms all possible causes and lists
As the investigation progressed the first 2 possibilities are eliminated leaving the 3rd and 4th as where the SIB needs to focus
Helps to isolate areas that need more investigation and shows you the rationale for the areas you have ruled out.
Determine what you need to look at to make a conclusion
This will take up a lot of white board space

## Slide 71: 3-Column List
What We Believe
What We Know
MA was KC-135
Mishap occurred at 1435L during a touch and go, 7 Oct
This is where most investigative efforts are being focused
- Left Main Landing Gear (LMLG) departed AC
- Crew left AC configured
- Crew safely recovered AC
- Fill hole bolt found loose, no safety wire installed
- Fill hole bolt loose, safety wire not installed before flight
- LMLG strut was serviced at some point prior to flight
- Improper servicing caused LMLG to depart AC
- Aircrew actions not a factor
What We Need To Know
- Last strut servicing date
- Who serviced the strut
- Interview
- What T.O. utilized to service
- What does it say specifically
about fill hole, safety wiring?
- Who signed off on the servicing?
- Interview
- Last major maintenance performed on strut?
- When, what was it?
- Interview crewmembers
- Any eyewitnesses to landing?
Notes: How it looked when applied to the 3 columns.
“What we know” are the facts………….
“What we believe” are the brainstorming and assumptions we have based on the evidence collected to date
“What we need to know” are the questions we need answered, interviews we need to accomplish, T.O.s we need to review etc., during the investigation.
Items typically move right to left across the columns as the investigation progresses.

## Slide 72: Factors
A factor is any deviation, out-of-the-ordinary or deficient action, or condition, discovered in the course of an investigation that contributed to the eventual outcome
Most mishaps involve multiple factors
    Example factors: (Factor Areas to Consider – SIB Go Package)
    Supervision
    Qualifications
    Weather
    Logistics
    Maintenance
    Mission Planning
    Flight Discipline
    Currency/Experience
    Etc.
Notes: First we need to determine the “factors” in the mishap………………
A factor is………………………(read the definition)
Factors: Enable the investigator to take the investigation from everything is on the table to these are the areas that are significant
DAFI 91-204:
8.5.1. Factors. A factor is any deviation, out-of-the-ordinary or deficient action, or condition, discovered in the course of an investigation that contributed to the eventual outcome. Determining factors (and eliminating issues that were not factors) enables investigators to focus the investigation from all the issues under examination to those specific areas that are significant in the event. Factors explain why causes, such as pilot error, supervision, or equipment failure occurred. Factors are not mutually exclusive but are often interrelated and in some cases influence each other. Factors are the basis for primary findings and recommendations. Most events involve multiple factors. The SIB will:
8.5.1.1. Ensure all Class A, B, and on-duty Class C mishaps contain at least one causal factor. (T-1) Refer to discipline-specific manuals for other event causal factor requirements. Ensure factors are written in narrative format and include detailed analysis of the actions or conditions that influenced the mishap. (T-1) Include enough information so the reader can logically follow the SIB’s rationale. (T-1) Include references to specific technical orders, publications, training, personnel actions or inactions, results of technical analysis, quotes from interviews, human factors, etc. (T-1) Use photos or diagrams as necessary.
8.5.1.2. When analyzing actions, organize factors as a discussion of how the action should have been accomplished, how it actually occurred during the mishap, and explain why there was a difference. (T-1) Then analyze how the difference between what should have occurred and what actually occurred affected the mishap. (T-1)
8.5.1.3. When analyzing conditions (e.g., weather, fatigue), explain how and why the condition influenced the outcome of the mishap. (T-1)
8.5.1.4. When analyzing publications (e.g., technical orders, AFIs), explain what the publication stated at the time of the mishap, how it was deficient, and how the deficiency contributed to the mishap. (T-1) Contrasting similar publications can be helpful in explaining why the publication was deficient.
8.5.1.5. Determine whether an action or condition was a factor or causal factor in the mishap. (T-1) If the SIB cannot narrow it down to a single most likely cause, the SIB will identify the alternatives and state “Action X most likely occurred due to one or more of the following reasons.” (T-1) Then list the reasons from most probable to least probable. (T-1) It is not necessary to list every single possibility.

## Slide 73: Factors
The pilot rushed his preflight due to extremely cold weather and failed to notice an engine cowling was left unlatched by maintenance personnel. The engine cowling opened during takeoff and damaged the leading edge of the wing.
      “PILOT ACTIONS” – Pilot allowed his preflight to be rushed
      “WEATHER” – Cold weather caused the pilot to rush his preflight
      “MAINTAINER ACTIONS” – MX failed to properly latch the cowling

## Slide 74: Factors
Operator 1 (OP 1) rolled a Humvee during an exercise which fatally injured the turret gunner. The weather was unremarkable, vehicle condition was not a factor, OP1 was properly licensed and trained. OP1 was noted for his aggressive, dangerous driving which had been discussed by his peers with the shift leader and his immediate supervisor. Peers had noted OP1 stated he wanted to "get the HMMWV on 2 wheels." No action was taken and the information was not relayed further up the chain.
      “UNIT SUPERVISION” – Failed to correct O1's driving behaviors
      ???
Notes: One is missing here…….how about OP1 being causal for aggressive, dangerous driving

## Slide 75: Factors
Trainer aircraft has an unrecoverable in-flight engine shutdown when the Instructor Pilot (IP) inadvertently pulls the throttle to cutoff at low altitude while reducing the power to idle. Poor throttle finger lift design allowed the possibility of inadvertent shutdown of engine. After ejection the pilot was unable to contact search and rescue due to survival radio battery failure.
      T.O.s fail to address the possibility of inadvertently cutting of the engine when using the throttle
      “AIRCRAFT DESIGN” – Throttle finger lift design allowed possibility of inadvertent shutdown of engine
Notes: What about the survival radio battery issue?

## Slide 76: Non- Factors Worthy of Discussion
Non-Factors Worthy of Discussion (NFWoD): Issues/deficiencies discovered during the investigation that did not influence this mishap
    Possible factors in the investigation thoroughly investigated but ruled out (e.g., bird strike in an engine failure mishap)
    Things we uncover during the investigation that did not cause the mishap or influence but should be fixed due to the potential to be a factor in a future mishap (e.g., failure of survival radio batteries)
    CA interest items (e.g., Risk Management (RM), Cockpit/Crew Resource Management (CRM))
Notes: Non-Factors Worthy of Discussion (NFWoD) Could fall into one of three categories:
Possible factors in the investigation that we ruled out (i.e. bird strike in an engine failure mishap)
Things we uncover during the investigation that did not cause the mishap or influence the outcome but that we want to have fixed due to the potential to be a factor in a future mishap (i.e. failure of survival radio batteries)
Commander interest items (like RM, CRM, etc)
DAFI 91-204:
8.5.2. Non-Factors Worthy of Discussion. Non-Factors Worthy of Discussion are written in narrative format and fall into one of three categories: areas that were thoroughly investigated and subsequently ruled out as factors (in order to provide context of why these areas are not factors), areas uncovered during the investigation that did not cause the event or influence the outcome but should be fixed due to the potential to be a factor in a future event (e.g., incorrect information in a technical order), and areas that may be considered an interest item to the Convening Authority (e.g., risk management, crew resource management). Non-Factors Worthy of Discussion are the source for Other Findings and Recommendations of Significance. Not all Non-Factors Worthy of Discussion result in Other Findings and Recommendations of Significance, but the SIB must have a corresponding Non-Factor Worthy of Discussion for each Other Findings and Recommendations of Significance. (T-1) The SIB will:
8.5.2.1. When analyzing areas that were ruled out as factors, explain what the SIB investigated and why they determined it did not influence the mishap. (T-1) Often the SIB will need to answer why other plausible scenarios were ruled out.
8.5.2.2. When analyzing areas that could be a factor in a future mishap, explain the deficiency and why it could lead to a mishap. (T-1)
8.5.2.3. When analyzing areas that may be considered an interest item to the Convening Authority use either of the methods described in paragraphs 8.5.2.1 and 8.5.2.2 as appropriate. (T-1)

## Slide 77
Report Writing
(Brief on or about Day 15)

## Slide 78: Safety Investigation Board The Report
AFSEC/SEFF
1 Aug 2023

## Slide 79: Overview
Exhibits
Narrative
  Factors
  Findings & Causes
  Recommendations
Notes: This is what we’ll cover

## Slide 80: SIB Deliverables
Brief to CA Final Message
Safety Report
Notes: 3 products the SIB will produce
Safety Report - Exhibits and data, which are entered into Air Force Safety Automated System (AFSAS), the AF’s computerized program of record for mishaps, recommendations, and mitigating actions.
  The briefing produced by the BP given to the convening authority at the conclusion of the investigation which is also entered into AFSAS as an exhibit within the “Safety Report”
  The final message (mishap narrative, findings, causes, recommendations, etc) which is also entered into AFSAS as part of the “Safety Report”
Although work on each of these will be occurring throughout the SIB process, days 21-30 is when we’ll be finalizing these products prior to deconvening and proceeding to the CA Out-brief.
DAFI 91-204: 8.11. Safety Reports. Detailed information about events are organized and assembled into safety reports. Safety reports consist of the approved final or final supplemental message, and all exhibits.

## Slide 81: Preparing the Exhibits
Notes: FOOT STOMP: Recorder and AFSEC Rep will focus efforts here. Recommend flowing the exhibits through the Recorder for review then to the AFSEC Rep (or IO if no AFSEC Rep) will upload the exhibit once QC’d against DAFI 91-204 and DAFMAN 91-223 requirements.
AFSAS is where we’ll input our exhibits, some are optional, some are required based on type/class of mishap.
Exhibits prepared IAW DAFI 91-204 Table 8.1 and DAFMAN 91-223 7.1.5 Managing Exhibits…REVIEW THOROUGHLY WHEN UPLOADING EACH EXHIBIT

## Slide 82: Investigation Flow
Mishap
Investigation
Factors
Findings
Causes
Recommendations
Determine and reconstruct the sequence of events
Any act or issue that affected the outcome of the mishap, whether causal or not
Mishap overview in chronological order containing factors and events that sustain the mishap sequence
Findings that explain why the mishap occurred
Report
Write the report
Feasible Actions which are intended to prevent recurrence of a similar mishap
Notes: Without regard to a timeline, here is how the investigation progresses
We have established the “what” and “why” of the mishap sequence
We should now be preparing to write out our detailed analysis to provide a complete picture to the reader of what happened and why it happened. (Day 20-30)

## Slide 83
Narrative

## Slide 84: Narrative
Most time consuming, detail-oriented phase
The Narrative is the heart and soul of the SIB process
  Factors/Findings/Recommendations “Meat” of the Narrative
  Expect between 15,000 to 20,000 words in length
  30 to 60 pages
Becomes the final message
Notes: Narrative is the report produced by the SIB documenting why the mishap occurred, findings, causes and recommendations.
The “tin kicking” portion of the SIB is over and it’s time to put pen to paper
Writing on this should have started in the days 11-20 period.
Length of the narrative will depend on the circumstance of the mishap, there is no set length.

## Slide 85: Narrative - Sources of Data
Narrative
Training Records
Tech Orders
Technical Teardowns
Interviews
MFOQA, RM
FDR/CVR
Notes: What Sources of data to compile for Narrative

## Slide 86: Preparing the Narrative
Reference DAFI 91-204, 8.5 - 8.10 and Discipline Specific DAFMAN for guidance on preparing the narrative
More an “art” than a “science”
    Use Narrative template/example provided in SIB Go Package
    Review the format and writing style
Responsibility of ALL SIB members to draft, but IO typically compiles
Notes: Guidance for the reports can be found in the applicable AFMANs
All SIB members will write their applicable section, IO’s job to compile
Problem with this is it becomes a document by committee with different writing styles.
Up front get folks to agree on certain writing ROE………………will make IO’s job easier
Come to consensus on what to call individuals involved in the mishap (MP, MC, MM1, W1 etc..)

## Slide 87: Preparing the Narrative
Sequence of Event
Investigation Conclusions
Background Information (Person, Object, General)
Factors (Causal Factors, Factors, NFWODs)
Primary Findings
Primary Recommendations
Other Finding of Significance, Other Recommendation of Significance (OFS/ORS)
Glossary of Terms and Acronyms
Referenced AFSAS Reports
Notes: This is how things will appear in the final message but not how it’s organized in AFSAS
Investigation conclusions will be written last
Each of these areas are data field inputs

## Slide 88: Preparing the Narrative
Comprised of:
  Factors that collectively answer the “why” an event occurred based on the weight of evidence, professional knowledge, and good judgment of the investigators
  The analysis that led to the findings and recommendations
  Potentially relevant factors considered and rejected, with detailed analysis to support rationale (NFWoDs)
Use illustrations to clarify if required
  A picture is worth a thousand words
Notes: It is important to remember to not only include what was ruled in and why with regards to being a factor in the mishap sequence, but what was ruled out and why. Explain the process used to arrive at the conclusions. If an issue could have “reasonably” been a factor in the mishap sequence but wasn’t, explain in the appropriate section how the SIB determined it wasn’t a factor. Not all non-factors need to be discussed as NFWODs. For example, if the SIB is dealing with a gear-up landing and during the course of the investigation determined that airfield NOTAMs were not an issue, that doesn’t warrant mention in the report. However, given the same gear-up landing, if the SIB determined that recent maintenance performed on the landing gear wasn’t a factor, that deserves discussion on how it was ruled out.
The use of illustrations can help to clarify SIB discussions……………..

## Slide 89: Preparing the Report Writing the Narrative
“The nozzle separated at the aft spot welds on the
augmentor duct …”
WHAT?!?!?!
Notes: For example……………………..
What is this top bullet trying to explain?
The use of illustrations can clarify in the readers mind what the SIB determined

## Slide 90: Writing
Factor Title (e.g., “Technical Data Compliance”)
Analysis: SIB method to determine the factor’s influence on the mishap scenario.
  Include enough information so the reader can logically follow the SIB’s rationale for conclusions reached.
  Should include references, as appropriate, to specific Technical Orders/Publications, training received, actions accomplished, results of technical analysis, etc.
Determination (Causal, Factor, NFWOD)
Notes: The format for writing the paragraphs in the Narrative
Emphasis Bullet:
Recurring weak area: Include enough information so the reader can logically follow the SIB’s rationale for conclusions reached.
SIBs do a great job explaining the “what” in the mishap sequence, often come up short in explaining “why”
SIBs have problems with this, show you how to overcome in a few slides
DAFI 91-204:
8.5.1. Factors. A factor is any deviation, out-of-the-ordinary or deficient action, or condition, discovered in the course of an investigation that contributed to the eventual outcome. Determining factors (and eliminating issues that were not factors) enables investigators to focus the investigation from all the issues under examination to those specific areas that are significant in the event. Factors explain why causes, such as pilot error, supervision, or equipment failure occurred. Factors are not mutually exclusive but are often interrelated and in some cases influence each other. Factors are the basis for primary findings and recommendations. Most events involve multiple factors. The SIB will:
8.5.1.1. Ensure all Class A, B, and on-duty Class C mishaps contain at least one causal factor. (T-1) Refer to discipline-specific manuals for other event causal factor requirements. Ensure factors are written in narrative format and include detailed analysis of the actions or conditions that influenced the mishap. (T-1) Include enough information so the reader can logically follow the SIB’s rationale. (T-1) Include references to specific technical orders, publications, training, personnel actions or inactions, results of technical analysis, quotes from interviews, human factors, etc. (T-1) Use photos or diagrams as necessary.
8.5.1.5. Determine whether an action or condition was a factor or causal factor in the mishap. (T-1) If the SIB cannot narrow it down to a single most likely cause, the SIB will identify the alternatives and state “Action X most likely occurred due to one or more of the following reasons.” (T-1) Then list the reasons from most probable to least probable. (T-1) It is not necessary to list every single possibility.

## Slide 91: Writing
Factor Title(e.g., “Technical Data Compliance”)
Analysis: SIB method to determine the factor’s influence on the mishap scenario.
Often it is advised to organize this section into a discussion:
  How the particular action should have been accomplished
    Best Practice: Quote guidance, training, standards, etc.
  How it actually occurred during the mishap
    Best Practice: Detail “What” happened
  Why the difference
    Best Practice: Detail “Why” it happened (tech analysis, interviews, human factors, weight of evidence – “most likely”, etc.)
  How this contributed to the mishap.
    Best Practice: SIB conclusion on how this led to the resultant damage, injuries, etc.
The last portion of each factor analysis will be a brief summary that ties the discussion together.
Notes: Emphasis Bullet:
Recurring weak area:
What should have happened/what’s the standard
What actually happened
How it contributed to the mishap and why the difference
Close with a tie-it-all-together statement
This analysis format makes the logic easy to follow and for the reader to come to the same conclusion
Technique: Write the first factor or NFWOD and then debrief it as a group with the AFSEC Rep (or IO if no AFSEC Rep).
DAFI 91-204:
8.5.1.2. When analyzing actions, organize factors as a discussion of how the action should have been accomplished, how it actually occurred during the mishap, and explain why there was a difference. (T-1) Then analyze how the difference between what should have occurred and what actually occurred affected the mishap. (T-1)
8.5.1.3. When analyzing conditions (e.g., weather, fatigue), explain how and why the condition influenced the outcome of the mishap. (T-1)
8.5.1.4. When analyzing publications (e.g., technical orders, AFIs), explain what the publication stated at the time of the mishap, how it was deficient, and how the deficiency contributed to the mishap. (T-1) Contrasting similar publications can be helpful in explaining why the publication was deficient.

## Slide 92: Writing
Be forewarned that it will take numerous writes and rewrites to get the Narrative to read the way you want it. Paragraphs will be written, then deleted, then reinserted with changes, deleted again, melded into a different section, etc. This is necessary to properly develop the Narrative.
In the early drafts, flush out concepts and flow, not grammar. Nothing will stop Narrative progress quicker than worrying about dangling participles, colons vs. semi-colons, one vs. two spaces after a period, etc. You miss the concepts and flow while working on grammar corrections. Save those for much later drafts of the Narrative.

## Slide 93: Writing
Problem Areas:
Where Did You Get The Information?
    Smith AFB now checks torque in accordance with T.O. procedures, (what is the T.O. reference for this torque check) during the 300 hour phase inspection.
    The SIB examined documentation of widget pin removal and reinstallation in the AFTO 781As. The investigation revealed the MA was towed four times, yet had no AFTO 781A documentation for pin removal/reinstallation. (Where does it say this is required? IAW what T.O. and paragraph #? If you’re going to say they’re not following guidance, be sure to give the references of what isn’t being followed)
Notes: ANOTHER WEAK AREA……………..WHERE DID YOU GET THE INFORMATION

## Slide 94: Writing
Writing to a narrow audience
    Write to the “village idiot”
Persuasive, complete, accurate writing
    You know what you mean
Notes: When the SIB wrote this paragraph it looked good to them.
Often times you’ve been so close to the investigation for so long, you write to your level of understanding
You know what you mean but those outside the investigation don’t.
Don’t be afraid to include too much detail, write to the village idiot

## Slide 95: Preparing Report: Problem Areas
Numerous drafts to get to final product
  Can’t see gaps in logic/info after awhile
Techniques to help overcome:
  Read aloud, keep one member out of the writing, etc.
  Step back, try to read the report like somebody who knows nothing about the mishap
  Take a day off from reading then re-attack
  Murder boards
  Convening Authority/SE
Notes: To help overcome this problem……………….
Keep one member out of the writing and let them QC the drafts (BP)
Step back, try to read the report like somebody who knows nothing about the mishap (someone from a different community)
You can also send a copy to Convening Authority/SE ask them QC what you’ve written

## Slide 96: Preparing Report: Problem Areas
DAFMAN 91-223:
  SIBs should forward draft copies of the narrative as soon as available to the CA Flight Safety Staff for review
  SIBs supported by AFSEC Rep (on-site or telephonically), should forward draft copies of the narrative to AFSEC/SEF for review
  Other SIBs may request a review through the AFSEC Flight Safety Investigations Branch (AFSEC/SEFF)
  This review should normally be requested on or before day 25 of the investigation
    The SIB should allow at least two duty days for the CA Flight Safety Staff and AFSEC/SEFF reviews
    These reviews ensure compliance with DAFI 91-204 and this DAFMAN
Notes: In fact, for flight, this is directed by the DAFMAN………….
Emphasis Bullet
Reviewing safety specialists are to provide suggestions for accuracy/effectiveness and do not supersede the judgment of the SIB/SIO.
They can not direct you to make changes, only offer suggestions
DAFMAN 91-223:
7.2. Class A and B SIB Safety Reports. SIBs should forward draft copies of the narrative as soon as available to the CA Flight Safety Staff for review. Additionally, SIBs supported by AFSEC (on-site or telephonically), should forward draft copies of the narrative to AFSEC/SEF for review. Other SIBs may request a review through the AFSEC Flight Safety Investigations Branch (AFSEC/SEFF). This review should normally be requested on or before day 25 of the investigation. The SIB should allow at least two duty days for the CA Flight Safety Staff and AFSEC/SEFF reviews. These reviews ensure compliance with DAFI 91-204 and this DAFMAN. They also ensure the analysis supports the SIB’s findings, cause(s), and recommendation(s). Narrative review comments should be shared between AFSEC and CA flight safety staffs. Reviewers may not direct SIBs to change their conclusions, but may direct SIBs to provide more analysis to support conclusions. Other than AFSEC involvement, the investigation will not be staffed outside of the CA safety office during this review process.

## Slide 97: Preparing Report: Problem Areas
Following an F-15 tire failure on takeoff Class A, CA/SE sent the following comments to SIB:
  No mention of what brand of tire failed (Goodyear vs Michelin), how many takeoffs/landings the tire had performed, was the tire new or recapped, what the actual condition of the tire was prior to takeoff
  Tire design is listed as a causal finding, but tire design is discussed as a non-factor worthy of discussion
  Inadequate discussion of who serviced the tires or what procedures were followed
  No analysis written to explain why only this one tire failed, assuming that many/all of the F-15s taking part in the surge had their tires serviced by the same person/people using the same procedures and all taxied about the same distance
Notes: An example of QC comments back to a SIB……………..
This represents just 4 of the 11 comments returned to the SIB

## Slide 98: Preparing Report: Problem Areas
What?
  “Both bolts on the PTS flange display 45 degree shear overload failure indicating an upward shear with an axial tension force event.”
  Translation: The damage to the PTS flange bolts was from impact forces, not rotational forces.
Leave out the gore
Often under perceived “time crunch” to complete
  Underestimate time to complete and # of drafts required
  Anticipate taking at least a week to accomplish
  When is it finished?
Notes: Leave “the pilot was fatally injured due to total body fragmentation” for the doc’s section
Enough to say pilot was fatally injured
Emphasis Bullets
Underestimate time to complete and # of drafts required
Anticipate taking at least a week to accomplish
SIB’s historically underestimate length of time it takes to accomplish
Takes about a week, and many drafts to complete

## Slide 99: Remember
A superbly written report can not do much to overcome a bad investigation but a poor report can definitely ruin a good investigation!
Rightly or wrongly, the report tends to be SIB’s “Report Card”
Notes: FOOT STOMP: The CA accepts the SIBs briefing on conclusions, findings, and recommendations primarily based on verbal/visual communications. The SIB must ensure that what is verbally and visually conveyed to the CA is also detailed textually in the final message and support in the safety report. If they do not match the brief, the report will not pass quality control reviews conducted by the CA/SE and/or AFSEC.
A poor report can definitely ruin a good investigation…….
You’ve got to be able to explain why the mishap occurred such that the readers can understand it and logically following your conclusions and why you made the recommendations you made.
SIB burnout phase is peaking during this period, your job is to keep folks energized
DAFI 91-204:
10.2. Convening Authority Quality Control Review. The Convening Authority’s safety staff will review the safety report before submitting the final message in AFSAS. (T-1) In addition, MAJCOM/FC safety staffs will review all Class A and B safety reports and NAF safety staffs will review all Class B safety reports. MAJCOM/FC and NAF safety staffs should perform reviews of other safety reports in their organization.
10.2.1. Report reviewers shall assess the entire report, including AFSAS database field entries, the final/final supplemental message, and all exhibits (both required and optional), to ensure investigative guidance and documentation standards established in this DAFI and in discipline-specific safety manuals are satisfied. (T-1) The review will ensure adequate evidence and analysis is presented to support the investigation’s conclusions, findings, and recommendations. (T-1) Reviewers will complete the Mishap Quality Control Checklist completed by the SIB and forward to the next level reviewer via e-mail or AFSAS file share. (T-1)
10.2.2. If any portion of the safety report, particularly the narrative, findings, causes, DoD Human Factors Analysis and Classification System codes, recommendations, and OPR and OCR responsibility assignments do not satisfy established requirements, safety offices shall return the safety report and work with the SIB to revise it until it meets established requirements. (T-1)
10.3. AFSEC Quality Control Review. AFSEC conducts a quality control review following the submission of a safety report.
10.3.1. The AFSEC review process will be accomplished within 10 business days of the submission of the safety report. (T-1)
10.3.2. Non-compliance items will be addressed by the SIB. (T-1) Once corrections are made the SIB will resubmit the final message. (T-1)
10.3.3. The Convening Authority will ensure the SIB addresses the results of the AFSEC review within 10 business days after the review is posted in AFSAS. (T-1)

## Slide 100: Human Factors
Human factors are analyzed by all SIB members.
Human Factors Analysis and Classification System (HFACS) is incorporated in AFSAS. It is used to categorize what human errors occurred. Major headings include:
  Unsafe Acts
  Preconditions
  Supervision / Leadership
  Organizational Influences
Notes: IN THE PAST, INVESTIGATORS HAVE THROWN HUMAN FACTORS ANALYSIS TO THE MEDICAL INVESTIGATOR AND HAVE ASKED HIM OR HER TO DO THIS WORK ON THEIR OWN. THIS PRACTICE HAS SOMETIMES PRODUCED HUMAN ERROR ANALYSES THAT DIFFERED CONSIDERABLY FROM THE BOARDS’ INVESTIGATION AND FINDINGS OF FACT. INTEGRATING HUMAN FACTORS ANALYSIS INTO ALL ASPECTS OF THE INVESTIGATION WILL RESULT IN A MUCH MORE COHERENT FINAL PRODUCT.
This is a sampling of the major headings and sub HFACS.

## Slide 101: Preparing the Report Human Factors
Integrate Human Factor (not to be confused with HFACS) terms directly into the Factor write-up to aid in describing human actions:
  “These actions coupled with communications from his flight lead, multiple position and altitude calls to regain element mutual support, monitoring of flight parameters, and maneuvering away from high terrain near the aircraft combined to produce a situation of cognitive task saturation resulting in the MP being fixated on his RPM gauge and never analyzing his EGT gauge.”

## Slide 102: Preparing the Report Human Factors
Info presented must be consistent
  Factor and AFSAS entered HFACS must agree
Get a Human Factors expert on the SIB if required
  Works with FS to determine Human Factor issues of mishap
  CA/SG is focal point
  AFSEC/SEH Division for advice
Help FS/HF expert see it from the operator/maintainer’s perspective
Notes: Factors AFSAS HFACS must agree
This is another SIB weak area

## Slide 103: Medical / Technical Speak …
Tone down the “Medical / Technical Speak”
  "Loss of the right lamina papyracea and opacification of the right ethmoid sinus are consistent with a right medial wall blowout fracture."
  Translation: The X-Ray shows the individual was struck in the right eye.
Notes: Tone down the Medical / Technical Speak
Doc language is different than general populace language
Engineering and test language is different than general populace language
This works for medical, engineering analysis, and test reports; dumb it down for narrative so the lay person can understand it.

## Slide 104: Findings, Causes & Recommendations
Notes: As we’re working on the narrative we’ll also start drafting findings, causes and recommendations

## Slide 105: Findings
FACTORS
FINDINGS
RECOMMENDATIONS
Notes: Factors become findings become recommendations.
The recommendations must be supported by the findings which must be supported by the factors

## Slide 106: Findings
Statements in chronological order of each single event or condition essential in sustaining the mishap sequence
Findings represent the SIB's conclusions after analyzing and deliberating all the facts, based on the weight of evidence, professional knowledge, and good judgment of the investigators
Start the sequence when the initial actions occurred, which may be prior to the day of the mishap (e.g., design problems, improperly written directives, an inadequate training)
Technique: Bulletize mishap overview (in complete sentences) in chronological order from the first event in the sequence to the end of the mishap sequence
  Retain the “factors” in the mishap
  Retain the essential events/conditions that sustain the mishap sequence
Notes: FOOT STOMP: Review DAFI 91-204, 8.7. Determining and Documenting Findings.
Technique: Bulletize (but in complete sentences) mishap overview in chronological order from the first event to the end of the mishap sequence
There are two types of findings:
  The “factors or essential steps” in the mishap sequence
  The events that sustain the mishap sequence (Start, taxi, takeoff…)

## Slide 107: Findings
List findings in time sequence, first to last
  When it occurred, not when discovered
  Design/T.O.s/Regulations/Training/Mishap
  Remember: Some events in the mishap sequence began long before the actual mishap:
    Finding 1: The Original Equipment Manufacturer produced the F-117 with an aircraft design that is highly conducive to spatial disorientation.
    Finding 1: The KC-135 Program Office accepted the F108 engine with a known design deficiency that predisposes the third stage fan disk lugs to fractures due to high cycle fatigue (HCF).
The sequence continues to the point where all damage or injury has occurred
Notes: As further defined in the 91-204 paragraph 5.10
After reading it is still tough to determine what exactly findings are/look like unless you’ve worked with them previously.
Emphasis Bullets
List findings in the order of when they occurred relative to the mishap sequence, not when discovered by the SIB
Some Event Sequences Begin Long Before the Actual Mishap Sequence With Design Problems, Improperly Written Directives, or Inadequate Training Program:
  Finding 1: The Original Equipment Manufacturer produced the F-117 with an aircraft design that is highly conducive to spatial disorientation.
  Finding 1: Finding 1: The KC-135 Program Office accepted the F108 engine with a known design deficiency that predisposes the third stage fan disk lugs to fractures due to high cycle fatigue (HCF).

## Slide 108: Findings
Each finding MUST be supported in a Factor
  For example:
  Finding 2: (Causal) Due to a lack of oversight, [Syllabus Owner] failed to ensure that Spatial Disorientation (SD) academic training is reinforced with “hands-on” SD simulation training.
  This must be discussed thoroughly within the analysis of the factor, in this case a “causal” factor
  Determination: Spatial Disorientation training was a Causal Factor
If it is not, the Factor was not written completely
Notes: FOOT STOMP:…………this finding is supported in Factor
Best Practice: To ensure they match, when finished with the Factor and Findings, lay them side by side and ensure what’s in the findings can be found in the Factor.
If not, need to edit the factor or the finding so they convey the same details.

## Slide 109: Findings
Do Not include events interesting to the reader but not necessary to sustain sequence
  For example:
  Scenario: Pilot was flying as an NVG instructor, not current to instruct NVG sortie, crashed during a non-NVG portion of the flight due to spatial disorientation
Where would you discuss this uncovered issue that did not cause the event or influence the outcome?
  Non-Factors Worthy of Discussion
Notes: These would lead to Other Findings and Recommendations of Significance we’ll discuss shorty.

## Slide 110: Findings
When the investigation cannot conclusively determine a specific causal action, list two or three of the most probable reasons based on evidence, professional knowledge, and judgment. For example:
  Finding XX: The mishap pilot failed to recognize a continuous shallow descent, most likely due to a combination of the following reasons: Channelized attention, Cognitive task oversaturation, Incorrect instrument-crosscheck
Notes: Despite your best investigative efforts, you may not know with 100% certainty why a mishap occurred
You’ll have a reasonable idea based on the evidence gathered and analyzed, but………………….
For example: a fatal mishap where the key witness can’t be interviewed to determine why they took the course of action they did.
In that case, we qualify the findings with words like “most likely” or “for an undetermined reason”
List the most likely reason first, etc..
DAFI 91-204:
8.6.7. Occasionally an investigator may not be able to conclusively determine a specific causal action. In these special cases, the investigator may choose to list two or three of the most probable causes for each option. In rare instances, the causal event may be unknown.
8.7.15. List as much of the sequence as can be supported when the SIB cannot pinpoint a correctable event. (T-1) List the reasons from most probable to least probable. (T-1) Show them as subordinate to the applicable finding by using a format such as "Action X most likely occurred due to one or more of the following reasons". Do not list all of the possible alternatives that could have existed merely because they cannot be eliminated. (T-1) Place this sort of conjecture in the factor analysis. (T-1)
DAFMAN 91-223:
7.1.2.6. During the mishap landing, the left main landing gear wheel departed the Mishap Aircraft (MA) most likely for one of the following reasons: improperly torqued locking nut, fatigue crack propagation in the axle, or axle materiel deficiencies.

## Slide 111: Findings
Before the first findings session:
  IO or AFSEC rep should draft initial set of findings based on discussions to date
As a rule of thumb, expect between 8-15 findings. If you've got more findings than that (typically SIBs have too many findings initially) it's likely some findings can be combined or deleted
Don’t confuse mishap severity with the number of findings required
Notes: Have the IO draft an initial set of findings based on the circumstances of the mishap and post them on the board prior to the first findings session…..
8 -15 findings is a good ballpark for the number findings, some will have more, some less.
The findings should be reviewed everyday by the SIB, as a group, until they are finalized

## Slide 112: Findings Example
The Scenario: An F-15 was on a red X for a hydraulic leak which required maintenance to replace the number one hydraulic gear box. During maintenance just prior to the mishap flight, a B-nut to the number one hydraulic gear box input side was under torqued because of ambiguous wording in the T.O.XXX, X.X.X. The T.O. does not present a specific torque setting but simply states “tighten two turns after hand tight is achieved.”
The aircraft took off, on departure the pilot got a number one engine fire light due to hydraulic fluid leaking from the under torqued B-Nut igniting in the engine bay. The pilot properly shutdown the engine IAW T.O. 1F-15A-1, declared an emergency and initiated an emergency return to the airfield.
Notes: Tell audience to read this and the following slide and we’ll demonstrate how it was used to build a set of findings

## Slide 113: Findings Example
On approximately a one mile final, tower called the pilot and requested the number of souls on board and fuel remaining. While answering the radio call the pilot allowed the aircraft to get slow which resulted in a high sink rate. The aircraft touched down in the overrun and the left main gear collapsed due to overload from the excessive sink rate which exceeded the design limited of the gear. With the left main landing gear collapsed the aircraft departed the left side of the runway approximately 1000 ft past the overrun and sustained Class A damage to the left wing. The pilot egressed uneventfully.

## Slide 114: The Scenario – Factors/Findings
What are the possible Factors in the mishap?
What would be the first Finding in the mishap?

## Slide 115: The Scenario – Factors
T.O. Guidance
Mishap Pilot’s Approach
Notes: Use existing handout – review rules

## Slide 116: The Scenario - Findings
Finding 1. The F-15 System Program Office published Technical Order (T.O.) XXX, X.X.X. with inadequate guidance with reference to the proper torque settings of hydraulic gearbox B-Nuts.
Finding 2. Following T.O. XXX, X.X.X guidance Mishap Maintainer 1 under-torqued the input side hydraulic line B-Nut on the number one hydraulic gear box during a gear box change.
Finding 3. At an unknown time, the under-torqued input side hydraulic line developed a leak in the engine bay.
Finding 4. Shortly after takeoff, the hydraulic fluid ignited in the #1 engine bay illuminating the #1 engine fire warning light.
Finding 5. The mishap pilot (MP) shut down the #1 engine in accordance with T.O. 1F-15A-1 and initiated an immediate emergency recovery.
Notes: Walk thru the findings, explain why each one exists (factor, sustains mishap sequence, etc.)

## Slide 117: The Scenario - Findings
Finding 6. On one-mile final the tower requested detailed emergency aircraft information.
Finding 7. Due to distraction from the radio call, the MP allowed the airspeed to become excessively low on final approach which resulted in a high sink rate.
Finding 8. The mishap aircraft (MA) touched down in the overrun and the left main gear sheared in overload as a result of the high sink rate.
Finding 9. The MA departed the runway and stopped in approximately 1000 feet, sustaining significant damage.
Finding 10. The MP egressed the MA without injury.
Notes: Walk thru the findings, explain why each one exists (factor, sustains mishap sequence, etc.)

## Slide 118: Causes
Causes are those factors/findings that singularly or in combination with other causes resulted in the damage or injury. According to DAFI 91-204, cause is:
  … a deficiency, which if corrected, eliminated, or avoided, would likely have prevented or mitigated the event damage or injury. In most instances a causal deficiency is correctable by commanders, supervisors, or individuals.
    Mishaps can have multiple causal factors and findings
    The intent of identifying causal parties in an investigation is to identify the point where corrective action is needed, not to place blame
Notes: After we determine the findings, we need to decide where cause fits in the sequence…which findings are causal
DAFI 91-204:
8.6. Determining and Documenting Causes. A cause is a deficiency which if corrected, eliminated, or avoided would likely have prevented or mitigated the event damage or injury. In most instances a causal deficiency is correctable by commanders, supervisors, or individuals.
8.6.1. Cause does not imply blame and it is therefore imperative to determine if a person’s performance or judgement was reasonable. If a person’s performance or judgment was reasonable considering the event circumstances, do not assign cause. It is not appropriate to expect extraordinary or unique superior performance in such cases.

## Slide 119: Causes
Publications or objects should almost never be found causal
    Rather, the party responsible for ensuring the publications are correct or the party responsible for ensuring an object does not fail with catastrophic consequences is causal, unless the party took all reasonably expected actions.
  Environmental conditions such as a bird strike, lightning, high wind, solar wind, meteorites, or flood may be causal only if all reasonable avoidance and damage/injury mitigation actions were taken.
Notes: DAFI 91-204:
8.6.4. Environmental conditions such as a bird strike, lightning, high wind, solar wind, meteorites, or flood may be causal only if all reasonable avoidance and damage/injury mitigation actions were taken.
8.6.5. The action that could have prevented a failure resides within the human realm and not on an object or publication. Publications or objects should almost never be found causal. Rather, the party responsible for ensuring the publications are correct or the party responsible for ensuring an object does not fail with catastrophic consequences is causal, unless the party took all reasonably expected actions. In such cases, there may be process or organizational failures, and appropriate parties may be identified as responsible for these failures.

## Slide 120: Causes
Findings which sustained the mishap sequence, but were normal to the situation (i.e., Expected Result), are not causal. For example …
    An engine failure occurring after a fuel boost pump failure is an Expected Result and not causal
CAUSE and EFFECT relationship
    Cause = “Why” it happened
    Effect = “What” happened
  Pilot over-Gs aircraft, wings depart
    Cause = Pilot over-G
    Effect - Wings departing
Notes: AGAIN, ONE OF THE MOST IMPORTANT CONCEPTS WHEN IT COMES TO IDENTIFYING AND DETERMINING ROOT CAUSE.
BOTTOM EXAMPLE
PILOT OVERG Gs A STRUCTURALLY SOUND AIRCRAFT AND THE WINGS COME OFF
DID THE WINGS COMING OFF CAUSE THE MISHAP OR THE OVER G?

## Slide 121: Causes
Apply the reasonable person, reasonable publications, reasonable parts concept when determining a cause
    If performance or judgment was reasonable considering the circumstances, do not assign cause
    If personal action was “reasonable” based on training received or published guidance, that action can not be causal, although deficient training or guidance might be
Notes: Be sure to look at “reasonableness” when determining cause.
Reasonable Person, Publications, Parts
This is very subjective. What is reasonable to you might not be to the rest of the SIB.
For example, lets say we’ve had 8 Class A F-16 nozzle loss mishaps. First one occurred 7 years ago. Dash-1 still contains nothing about how to fly the aircraft minus the augmentor nozzle. Is this reasonable?
After the first mishap, it probably would be reasonable because we would never expect the augmentor to fall off the aircraft.
Seven years, and 8 Class A mishaps later is it still reasonable?
DAFI 91-204:
8.6.1. Cause does not imply blame and it is therefore imperative to determine if a person’s performance or judgement was reasonable. If a person’s performance or judgment was reasonable considering the event circumstances, do not assign cause. It is not appropriate to expect extraordinary or unique superior performance in such cases.

## Slide 122: The Scenario Where Would You Place Cause?
Finding 1. The F-15 System Program Office published Technical Order (T.O.) XXX, X.X.X. with inadequate guidance with reference to the proper torque settings of hydraulic gearbox B-Nuts.
Finding 2. Following T.O. XXX, X.X.X guidance Mishap Maintainer 1 under-torqued the input side hydraulic line B-Nut on the number one hydraulic gear box during a gear box change.
Finding 3. At an unknown time, the under-torqued input side hydraulic line developed a leak in the engine bay.
Finding 4. Shortly after takeoff, the hydraulic fluid ignited in the #1 engine bay illuminating the #1 engine fire warning light.
Finding 5. The mishap pilot (MP) shut down the #1 engine in accordance with T.O. 1F-15A-1 and initiated an immediate emergency recovery.
Notes: Returning to the scenario, where would you put causal?

## Slide 123: The Scenario Where Would You Place Cause?
Finding 6. On one-mile final the tower requested detailed emergency aircraft information.
Finding 7. Due to distraction from the radio call, the MP allowed the airspeed to become excessively low on final approach which resulted in a high sink rate.
Finding 8. The mishap aircraft (MA) touched down in the overrun and the left main gear sheared in overload as a result of the high sink rate.
Finding 9. The MA departed the runway and stopped in approximately 1000 feet, sustaining significant damage.
Finding 10. The MP egressed the MA without injury.

## Slide 124: The Scenario Where Would You Place Cause?
Finding 1. (Causal) The F-15 System Program Office published Technical Order (T.O.) XXX, X.X.X. with inadequate guidance with reference to the proper torque settings of hydraulic gearbox B-Nuts.
Finding 2. Following T.O. XXX, X.X.X guidance Mishap Maintainer 1 under-torqued the input side hydraulic line B-Nut on the number one hydraulic gear box during a gear box change.
Finding 3. At an unknown time, the under-torqued input side hydraulic line developed a leak in the engine bay.
Finding 4. Shortly after takeoff, the hydraulic fluid ignited in the #1 engine bay illuminating the #1 engine fire warning light.
Finding 5. The mishap pilot (MP) shut down the #1 engine in accordance with T.O. 1F-15A-1 and initiated an immediate emergency recovery.

## Slide 125: The Scenario Where Would You Place Cause?
Finding 6. On one-mile final the tower requested detailed emergency aircraft information.
Finding 7. (Causal) Due to distraction from the radio call, the MP allowed the airspeed to become excessively low on final approach which resulted in a high sink rate.
Finding 8. The mishap aircraft (MA) touched down in the overrun and the left main gear sheared in overload as a result of the high sink rate.
Finding 9. The MA departed the runway and stopped in approximately 1000 feet, sustaining significant damage.
Finding 10. The MP egressed the MA without injury.

## Slide 126: Recommendations
Recommendations

## Slide 127: Recommendations
Effective recommendations that prevent future mishaps are the reason the SIB is convened, the most important outcome of the investigation
Take the time to get them correct
Notes: Effective Recommendations will prevent future mishaps…………

## Slide 128: Recommendations
Recommendations are feasible and effective solutions to eliminate identified hazards, or if the hazard cannot be eliminated, to mitigate the hazard’s potential consequences
Recommendations should target one or more of the hazards identified and documented during the investigation
All mishap investigations should include recommendations to prevent future mishaps
Notes: Next we’ll determine the recommendations aimed at preventing future mishaps.
Recommendations are defined as…………..(read slide)
Recommendations must relate to the findings, causal or not causal, in the mishap sequence.

## Slide 129: Developing Recommendations
To eliminate or mitigate the identified hazards consider the system safety “Order of Precedence” concept:
  Design (Implement a fixed gear)
  Incorporate Safety Devices (Implement an auto-extend system)
  Provide Warning Devices (Implement cockpit warning lights)
  Develop Training and Procedures (Improve the checklist or its use via training with instructors and in simulators. Mandate use of personal protective equipment)
Notes: Consider the four methods listed for developing recommendations. From top to bottom;
design – longest timeline, normally most effective, most expensive;
Develop training procedure – least effective shortest time
May recommend long term design recs and other interim recs for mitigation until the hazard is designed out
DAFI 91-204:
8.9.2. All recommendations should target one or more of the hazards identified and documented during the investigation. It is also sometimes prudent to make two or more recommendations against one hazard. Developing sound recommendations also requires recognition of the system safety "order of precedence" concept (design changes, safety devices, warning devices, and then training and procedures) which recognizes that not all risk mitigation alternatives are equal. SIBs will use the order of precedence to develop risk mitigation alternatives. (T-1)
8.9.3. Based upon the specific information discovered during the investigation, selected alternatives should be formulated into feasible and effective recommendations and other alternatives discarded. The purpose of using the “order of precedence” is to ensure investigators consider the entire range of available options and not just the cheap and easy ones.

## Slide 130: The Scenario – Possible Recommendation Areas
Fix the ambiguity in the T.O.
Require the B-nut be safety wired
Notes: These are the recommendations that would have come from the depot findings/causes example we built……………..
Avoid making do your job recs……….

## Slide 131: Recommendations
Recommendations should require the action agency to correct a deficiency rather than to implement a particular solution
  POOR: Move the right engine fire shutoff switch to the right side of the cockpit.
  BETTER: Implement changes to the F-15E engine fire push-buttons to preclude incomplete engine shutdowns.
Notes: FOOT STOMP: Review DAFI 91-204, 8.9. Determining and Documenting Recommendations.
The action agency normally has greater expertise than the investigators and should be given the opportunity to develop the optimal solution for a problem.

## Slide 132: Recommendations
Do not write recommendations that only require a study or evaluation (evaluations are implicit in the process)
  POOR: Evaluate changes to the brake anti-lock system.
  BETTER: Implement changes to the F-16C/D brake anti-lock system to prevent loss of feedback.
Notes: In most cases, it is not necessary to recommend a study or evaluation, since studies or evaluations are implicit in the process.
Again for a complete listing of recommendations guidance, review DAFI 91-204 para 8.9.
Best Practice: Review 91-204, 8.9 after writing recommendations to ensure they are in compliance with guidance.

## Slide 133: Recommendations
Recommendations should be “closable”
  POOR: Conduct refresher training of all depot maintenance personnel emphasizing proper tool control procedures.
  POOR: Train contractor technicians to utilize data logger information in troubleshooting in-flight problems.
  BETTER: Change AFI 21-101 to require annual refresher training of depot maintenance personnel on proper tool control procedures.
Notes: BULLET ONE AND TWO: IS THIS ONE TIME TRAINING OR ANNUAL? IF ANNUAL HOW CLOSE (WRITE INTO GUIDANCE AS ANNUAL REQUIREMENT)

## Slide 134: Recommendations
Make sure recommendations wording can stand alone to be understood
  Perform a One-Time inspection (OTI) on the remaining aircraft in the B-1 fleet.
  Inspection of What?
Notes: This recommendation related to other recommendations made for the same mishap, but if the other recommendations aren’t reviewed at the same time, what does this mean?

## Slide 135: Recommendations OPRs
If a recommendation requires funding to effect changes, assign to the appropriate office within the lead command as the Office of Primary Responsibility (OPR)
If another organization is responsible for performing or managing the work, assign these organizations as the Office of Collateral Responsibility (OCR)
Recommendation X: Implement changes to the F-16 brake system to reduce the probability of encountering “hot brake” temperatures.
  OPR: ACC/A8 OCR: AFLCMC/LAB
ACC/A8 would be responsible to arrange for the prioritization and funding.
AFLCMC/LAB would either perform the required work or manage the contracted effort.
Non-AF OPRs
Notes: One of our major challenges when writing recommendations is to indentify the OPR who will be tasked to execute the recommendation.
Some actions can be taken at unit level. Other recommendations require MAJCOM or other agency actions
Basic ROE…………..(see slide)
If funding is involved it usually comes back to lead command for the MWS.
ACC is the lead command for the F-16, not PACAF or ANG
ACC would be the OPR for F-16 modifications.
Some recommendations are handled at the unit level.
Reducing the bird strike hazard at base X following a bird strike Class A mishap would usually fall to the local unit (fix the drainage ditches where birds gather, etc)
Non AF OPRS: Sometimes the responsibility for a recommendation lies outside the Air Force (e.g., the FAA for various air traffic control issues). Since the Air Force may not have the authority to task such agencies to perform recommended actions, do not assign non-Air Force agencies as OPRs or OCRs. In these cases, write the recommendation as an Air Force action and assign the appropriate Air Force organization as OPR. This Air Force organization is typically responsible for interaction with or contractual oversight of the outside agency and will ensure proper recommendation evaluation and disposition. Assign OCRs as required.
Emphasize
SIB/SIO is responsible for coordinating all recommendations with their proposed action agencies (OPR and OCR).
Ensure the correct OPR and OCR(s) are identified through positive contact (call or email them) prior to publishing the formal report or final message.
Include the office symbol, DSN/commercial telephone number, and email address of one OPR action officer for each recommendation. Place this information in the dedicated data field provided by AFSAS.
Contact the convening authority safety office to ensure proper action agencies have been identified.

## Slide 136: Recommendations OPRs
Perform a risk analysis for continued operation of KC-135, F108 stage one fan disk with possible high cycle fatigue (HCF) fracturing of the fan disk lugs and place restrictions or implement inspections on the fan disks as required.
  OPR?
Prior to resuming Night Vision Goggle (NVG) hoist operations, develop and implement HH-60 Standard Operating Procedures (SOP)/Tactics, Techniques and Procedures (TTPs) for NVG hoist operations.
  OPR?
Notes: How would you determine the OPR for these recommendations?
AFLCMC 135 engines would be a good place to start,,
Second tasks the contractor…..who works directly with the contractor?
OPR: ACC/A3T

## Slide 137: Recommendations OPRs
Limit OPR and OCR assignment to two or three-digit organizational levels to ensure proper management level attention
An OPR is required for each recommendation
List only one OPR per recommendation
Not all recommendations require OCRs
Notes: OPR ROE

## Slide 138: Recommendations OPRs
SIB/SIO is responsible for coordinating all recommendations with their proposed action agencies (OPR and OCR). Ensure the correct OPR and OCR(s) are identified through positive contact (call or email them) prior to publishing the final message
Include the name, rank, office symbol, telephone number, and email address of one action officer for the OPR and OCR (if designated) for each recommendation. Place this information in the dedicated data fields provided by AFSAS
The CA safety staff will ensure the SIB/SIO has made positive contact with the OPR and OCR(s)
Notes: FOOT STOMP: Coordination with the OPR and OCR is imperative to ensure the recommended action effectively eliminates/mitigates the hazard/deficiency the SIB uncovered in the investigation.
Wrong OPR designation and/or poorly written recommended action increases probability for closure during MOFE Review or closure without action.
Don’t just shoot in the dark and hope you got the correct OPR for a proposed recommendation…….point to circle, explain remainder of slide
This can serve a couple purposes…….
AFSAS will fail validation without all required OPR/OCR data
Help QC wording of Rec
Ensure have correct OPR or point you in direction of correct OPR
Gives them a heads up REC is coming their way
If in-depth discussion is required with OPR have them sign NDA

## Slide 139: Risk Hazard Indices/ Residual Risk
Baseline Risk Hazard Index (BHI)
    Baseline Severity
    Baseline Probability
Residual Risk Hazard Index (RHI)
    Residual Severity
    Residual Probability
Determines overall Risk Indices and Risk level
Drives prioritization and funding decisions
Reference the Narrative Template for BHI/RHI procedures

## Slide 140: In Closing.…
To help you navigate
the process there
is a Class A
and Class B
SIB Techniques
Guide in AFSAS
“Pubs & Refs”
Notes: To help you navigate the process there is a Class A and Class B SIB Techniques Guide in AFSAS under “Pubs & Refs”